Osborne 01 / BYE510 / Smart Modem

     The   insert  for  the   Osborne,   B5OS-2.INS, 
describes  a hardware modification to  the  computer 
which I was able to avoid.  Since I am using a smart 
modem  it is possible to let it control BYE as  well 
as  the  phone connection.  Pin four of  the  serial 
connector  of  the Osborne is checked by BYE.COM  to 
determine if the modem is on line.  When this pin is 
at plus 5 volts or greater, the on-line condition is 
indicated. (my modem pulls pin four to plus 12 volts 
when  it  answers) When the caller hangs up  or  the 
line  is  lost,  the  modem grounds  pin  four.  BYE 
detects the ground at pin four and recycles,  making 
itself ready for the next call.  If your modem has a 
suitable  signal which you can connect to  pin  four 
you  are in business.  It looks like DATA SET READY, 
pin six on the modem,  might work.  I had previously 
modified my modem to bring the off-hook led  voltage 
to  the connector.  This provided the needed  signal 
and   I  was  able  to  get  BYE  running  with   no 
modification to my Osborne.

     When  a disconnect is caused by a  time-out, or 
when  the  caller  types  the  command  BYE,  it  is 
necessary  to run a program which commands the modem 
to disconnect.  When the modem disconnects, pin four 
will go to ground and BYE will recycle. BYE provides 
the option of running a program upon exit by setting 
the EXFILE equate to YES. My exit program sends a ^T 
to the modem,  delays one second to allow the  modem 
time  to abort,  and returns to BYE.  The program is 
named  PEXIT.COM and is on the same disk as  BYE.COM 
in  user area 14.  These options are selected by the 
equates EXFILE,  EXDRV,  and EXUSR.  In addition the 
following two equates must be set to NO:  PRNTGB    
                                          BYHANG    

     Using  a program to abort the modem solves  two 
other problems.  I keep BYE.COM on drive A.  What if 
the  caller decides to terminate the call and  types 
BYE  when logged on drive B?  I have a copy  of  the 
exit  program on drive B which I have named BYE.COM. 
If the caller types BYE while on drive B,  the  exit 
program  will send the abort character to the  modem 
and  BYE  will recycle just as  before.  The  second 
problem  involved  getting  BYE to  recycle  if  the 
caller was unable to enter the correct password. BYE 
has  an option for a user password but I decided not 
to  use  it.  I  wanted more options so  I  wrote  a 
password  program that is run when the phone line is 
first  picked up.(See equates  COMFILE,  COMDRV  and 
COMUSR) If the caller is unable to give the password 
the program sends a ^T to the modem. If the password 
is  correct the program sets the wheel byte  to  the 
value assigned that password. 

     After inserting B5OS-2.INS into BYE510C.ASM, be 
sure  to  check all the equates to insure that  they 
are  set correctly for your  system.  After  setting 
EXFILE  to yes you will also have to select the user 
area  and a file name.  The file name will  have  to 
match the exit-file  file name of the BBS equate you 
set to YES. File names appear in file control blocks 
toward the end of the BYE asm file. I am not using a 
BBS  program but I had to set the equate for one  of 
them to YES to avoid assembler errors.  My exit file 
name  and my entrance file name match the names used 
by that BBS system.


;PEXIT.ASM for use with BYE510
;for OSBORNE 01  bios 1.4
;Causes modem to abort by sending a ^T via the serial port
TURNOFF EQU     14H ;^T to abort modem - put your abort char here 
SHADOW  EQU     4000H   ;must be above 4000h
MEMREG  EQU     0EF08H 
CONT    EQU     2A00H   ;serial status/control
CNT1    EQU     0FFH    ;for delay loop
CNT2    EQU     0FFFFH  ;for delay loop
CNT3    EQU     04H     ;for delay loop
        ORG     100H
        LXI     D,BYBY
        MVI     C,9
        CALL    5
        JMP     DOBLK
BYBY:   DB      0DH,0AH,'GOOD BYE.....',0DH,0AH,24H
DOBLK:  LXI     H,BLKSTART
        LXI     D,SHADOW
        LXI     B,BLKEND-BLKSTART
        DB      0EDH,0B0H
        JMP     SHADOW
BLKSTART:       EQU     $       ;ends up at 4000h
        DI
        OUT     0       
        MVI     A,0     
        STA     MEMREG
        MVI     A,TURNOFF
        STA     CONT+1
        OUT     1
        MVI     A,1
        STA     MEMREG
        EI
        MVI     D,CNT3
LONG:   MVI     E,CNT1  ;one second delay to allow
SHORT:  LXI     B,CNT2  ;modem time to abort
LP1:    MOV     A,C
        DCR     A
        MOV     C,A
        JNZ     LP1
LP2:    MOV     A,B
        DCR     A
        MOV     B,A
        JNZ     LP2
        MOV     A,E
        DCR     A
        MOV     E,A
        JNZ     SHORT
        MOV     A,D
        DCR     A
        MOV     D,A
        JNZ     LONG
        RET
BLKEND  EQU     $
        END
;
                       <eof>