Data Structures Used in IBM PC Compatibles and the PS/2


                       Compiled and Annotated by
                         (c) 1985,'86,'87,'88

                  Send comments or corrections to:

                          William C. Parke
                          1820 S Street NW
                       Washington, D.C. 20009



----------------------------------------------------------------------------

The following data structures are found in RAM, ROM, on the boot sector
of formated disks, in file headers, or are created dynamically by the
operating system.  The structures establish the fields and parameters
needed by the operating system to initialize and maintain communication
with the various devices or files attached to the system.

_____________________________________________________________________________
-----------------------------------------------------------------------------
PC Data Format:
-----------------------------------------------------------------------------
Bit    = One or zero value.  A bit can be saved as an electrical circuit
         latch, through electrical capacitance, by an induced magnetic field,
         mechanical change, etc.  All information can be stored as a series
         of bits. Use DBIT for asm directive.

      Common Synonyms to bit values:

  1 = One  Set   High True  Yes On  Full Mark  Open  Pass  Start Active
  0 = Zero Reset Low  False No  Off Null Space Close Block Stop  Inactive

Nibble = Four bits, labeled 3 to 0; Half a byte; Used to store a
         numerical value from 0 to 9 in Binary Coded Decimal; Used
         to store hex value 0-F. (Also called nybble)

BCD    = Binary coded decimal value stored in one nibble as a value between
         0 and 9.  The 80x86 has several instructions for transforming
         between binary and BCD.

Tribble = Three nibbles; Used in MS-DOS File Allocation Table when the
         disk partition has less than 16 Megabytes.

Byte   = Eight bits, labeled 7 to 0.  Each ASCII character has a unique
         byte value. The IBM extended character set and the IBM EBCDIC
         characters have a unique byte value. The 80x86 registers AH, AL,
         BH, BL, CH, CL, DH, DL each hold one byte.  80x86 memory is
         accessible at a byte level. Use DB for asm directive.

ASCII Byte = American-Standard-Code-for-Information-Interchange byte.
         ASCII codes represent numbers, letters, symbols and controls
         using a 7-bit code.



EBCDIC = Extended binary coded decimal information codes established
         and used within IBM mainframe computers to represent numbers,
         letters, symbols and controls using an 8-bit code.

Packed Decimal = Bytes holding a decimal value (0-9) in each nibble.

Word   = Two bytes, sixteen bits, labeled 15 to 0.  The 80x86 registers
         AX, BX, CX, DX, SI, DI, BP, ES, DS, SS, and SP hold one word.
         The 80x86 memory is accessible at a word level.  An 80x86 word
         is stored low byte first.  Integer words use bit 15 for the
         sign.  A 'word' on some computers refers to a value which can
         be stored in an arithemetic register of the Central Processing
         Unit (CPU). Thus, the bit size of a word varies among computers.
         Use DW for asm directive.

Double Word = Two words.  The 80x86 memory can be addressed by a double
         word.  The 80x86 can load a double word from memory by a single
         instruction.  Double words are stored low word first.  Integer
         double words use bit 31 for the sign.  The 8087 stores the
         two's complement if the number is negative (i.e. 1 + NOT x).
         In this way, a number plus its negative becomes zero. Use DD
         for asm directive.

80386 Pointer = 48 bits.  Largest address pointer in 80386.  Use DP for
         asm directive.

Quad Word = Four words. Allocation for a long integer. Use DQ for asm
         directive.

Ten byte = Allocation for packed decimal.  Use DT for asm directive.

8087 Long Integer = 8 bytes, with last bit labeled 63 carrying the sign:
         If the number is positive, bit 63 is 0.  If negative, the
         two's complement of the number is stored, making bit 63 a 1.

8087 Packed Decimal = 10 bytes; bit 79 is sign, 78-72 unused, 71-0 are
         18 consecutive 4-bit packed decimal values.

8087 Short Real = 4 bytes; bit 31-23 is biased exponent (exponent + 127);
         22-0 holds normalized significand (shifted to left until 1
         appears at bit 23).  Bit 23 of number is implicit = 1.

8087 Long Real  = 8 bytes; bit 63 is sign of number; 62-52 is biased
         exponent (exponent + 1023); bits 51-0 are normalized significand
         (bit 52 of number is implicit = 1).

8087 Temporary Real = 10 bytes; bit 79 = sign; 78-64 = biased exponent
         (exponent + 16383); bit 63-0 = normalized significand, with
         explicit 1 at bit 63.

MASM Long Real DQ = 8 bytes; bits 63-56 = biased exponent (exponent + 129);
         bit 55 = sign; bits 54-0 = normalized significand with implicit
         1 as bit 55.

MASM Short Real DD = 4 bytes; bits 31-24 = biased exponent (exponent + 129);
         bit 23 = sign; bits 22-0 = normalized significand with implicit
         1 as bit 23.

Paragraph = 16 bytes; Change of address if an 80x86 segment register
         is incremented.

Page = 256 bytes; Change of address if an 80x86 register high byte
         is incremented.

Sector = 512 bytes; Smallest number of bytes which can be loaded by
         MS-DOS from a disk.

Cluster = A group of sectors which are indexed by MS-DOS as allocation
         units; these are reserved for file storage and data on disks.

Allocation Unit = Cluster which has been assigned in a File Allocation
         Table (FAT) for a disk.

Kilobyte = 1024 bytes (2**10); Smallest number of bytes in one
         allocation unit for a file under MS-DOS.

Segment = 65,536 bytes (2**16); 80x86 address range for fixed segment
         register; this range reached by an offset stored in a word
         register; The largest address space for an 8080 CPU.

Megabyte = 1,048,576 bytes (2**20); The largest address space for an
         8086 CPU; An 80286 can address 16 Megabytes of physical memory;
         An average book stores about 1 Megabyte of data in 250 pages.

Gigabyte = 1,073,741,824 bytes (2**30); An 80386 can address 4 Gigabytes
         (2**32) of physical memory; A laser disk can hold close to
         1 Gigabyte of data; 1000 books of information.

Terabyte = 1,099,511,627,520 bytes (2**40); The virtual address space of
         an 80386 CPU is 64 terabytes (2**46); Storage in a large library
         is under a terabyte; Estimated storage capacity of the human brain
         is about 10 terabytes.

_____________________________________________________________________________
-----------------------------------------------------------------------------
Disk Drive Structures:
-----------------------------------------------------------------------------
Diskette Control Table:
-----------------------------------------------------------------------------
The diskette control table address is stored in the Int 1Eh vector.  It
is used to establish diskette controller parameters during formating,
reading, and writing to a disk.  See Int 13h, function 18h.

 Table Definitions:

 Offset  Data type Description

  00H    BYTE      Disk Controller Mode byte 1:
                   ssssuuuuB     s=0-FH  = head step rate in milliseconds
                                 u=0-FH  = head unload time in milliseconds
  01H    BYTE      Disk Controller Mode byte 2:
                   llllllldB  l=0-7FH = head load time/2-1 in milliseconds
                                 d=0-1   = DMA flag (0 means DMA is used)
  02H    BYTE      Clock Ticks until motor off
  03H    BYTE      FM or MFM Mode:  Log2 (Bytes per Sector/128)
                    FM= Freq. Modulation used on single-density disks
                    MFM=Modified Freq. Modulation used on double-sided disks
  04H    BYTE      Last Sector on Track (e.g. 09H)
  05H    BYTE      Gap Length in Bytes
                    MFM   Bytes/Sector   Sectors/track  Write Gap  Format Gap
                      1           256             12H      0AH          0CH
                      1           256             10H      20H          32H
                      2           512             08H      2AH          50H
                      2           512             09H      1BH          6CH
                      3          1024             04H      80H          F0H
                      4          2048             02H      C8H          FFH
                      5          4096             01H      C8H          FFH
  06H    BYTE      Disk Data Length (80H for 128 bytes/sec or 0FFH otherwise)
  07H    BYTE      Gap Length when formatting
  08H    BYTE      Data pattern used during formatting (fill byte)
  09H    BYTE      Floppy Head Bounce Delay (in milliseconds)
  0AH    BYTE      Floppy Motor Start Delay (in 0.125 second intervals)
  0BH    BYTE      Floppy Motor Stop Delay (in 0.25 seconds intervals)

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Fixed Disk Drive Parameter Tables:
----------------------------------------------------------------------------

The address for these tables are stored in the Int 41h vector address
for drive 1, and Int 46h vector address for drive 2.  These tables can
be initialized to new drive type characteristics using Int 13h, function
9h.

 Offset Data type  Description

  00H    WORD      number of tracks (called cylinders on fixed disks)
  02H    BYTE      number of heads
  03H    WORD      start cylinder for reduced write current
  05H    WORD      start cylinder for write precompensation on inner tracks
  07H    BYTE      maximum number of bits to correct data errors
                   (ECC burst length; ECC=Error correcting code)
  08H    BYTE      controller options 7 disable access retries
                                       6 disable ECC retries
                                     5-3 000 (non-XT:
                                             5=defect map at max.cyl.+1
                                             3=more than 8 heads on AT)
                                     2-0 000   3 usec/step
                                         100 200 usec/step
                                         101  60 usec/step (approx.)
                                         110   3 msec/step
                                         111   3 msec/step
  09H     BYTE      time out value for read/write
  0AH     BYTE      time out value for format
  0BH     BYTE      time out for disk diagnostics
  0CH     WORD      landing zone
  0EH     BYTE      sectors/track
  0FH     BYTE      reserved

_____________________________________________________________________________
-----------------------------------------------------------------------------
BIOS System Structures:
-----------------------------------------------------------------------------
Hard Disk Primitive Boot Sector:
-----------------------------------------------------------------------------

Rather than a DOS Boot Sector, a hard disk may contain a primitive boot
sector which is loaded into memory by the system ROM as the first disk
activity.  This sector must be the first sector on the disk (cylinder 0,
head 0, sector 1).  It is loaded at 0:7C00H and then run, starting at
0:7C00H. The code and data from this sector is strongly machine
dependent. For IBM machines, the code checks the first byte of the four
16 byte disk drive partition tables starting at 01BEH to find the
designated active and bootable partition.  If one is not found, an Int
18h is generated to enter ROM BASIC.  Otherwise, the active DOS boot
sector is loaded and run.

 Offset Data type  Description

 000H   n BYTES    Primitive Boot Code to find active DOS partition
 1BEH   16 BYTES   First disk drive partition table
 ...
 1FEH   WORD       AA55H = boot record signature
-----------------------------------------------------------------------------
Extended Fixed Disk Drive Parameter Table:
-----------------------------------------------------------------------------

For PS/2 (except Model 30), the fixed disk sector 2 at Head 0, Track 0
contains the information needed to support DOS extended partitions, from
logical drive D: to F:.  The format is:

 Offset Data type  Description

 000H    1 WORD    Length of Extended Fixed Disk Drive Parameter Table below
 002H    22 BYTES  (ID) ASCII string: 'IBM HARDFILE TYPE xxx '
 018H    1 BYTE    Drive Type number in binary
 019H    16 BYTES  Fixed disk drive partition table
-----------------------------------------------------------------------------
Disk Drive Partition Table:
-----------------------------------------------------------------------------
The disk drive partition tables begin at offset 1BEH in the boot record
of the hard disk (track 0, cylinder 0, sector 1), at offset 019H in the
extended fixed disk drive partition table, and offset 1BEH in the DOS
boot sector.

 Offset  Data type Description

  00H    BYTE      Partition status: 00=inactive; 80H=bootable and active
  01H    BYTE      Starting head of boot code
  02H    WORD      Starting sector and cylinder of boot code
                    (cyl. = bits 15,14,7-0; sector = bits 13-8)
  04H    BYTE      Partition type: 1 = DOS with 12 bit FAT
                                   4 = DOS with 16 bit FAT
                                   5 = extended DOS
                                   6 = reserved
                                 0DBH= concurrent DOS
  05H    BYTE      Ending head
  06H    WORD      Ending sector and cylinder
  08H    DWORD     Starting absolute sector for partition
  0CH    DWORD     Number of sectors

The 16 byte block repeats for each of four partitions, until:

  40H    WORD      AA55H = valid boot record signature (at 1FEH)
which completes the first sector on the disk.

----------------------------------------------------------------------------
DOS Boot Sector:
-----------------------------------------------------------------------------

 Offset  Data type Description

  00H    3 BYTES   jump instruction to boot code in sector: JMP 0BH + nn
                   (near JMP for DOS 2.1 (E9H), short JMP for DOS 3.x (EBH) )
  03H    8 BYTES   Original Equipment Manufacturer (OEM) name and version
  0BH    nn BYTES  Bios Parameter Block as below
         bb BYTES  Boot Code
 1BEH    64 BYTES  Possible Partition Tables
 1FEH    WORD      AA55H boot signature
 200H    ...

----------------------------------------------------------------------------
Disk BIOS Parameter Block:
-----------------------------------------------------------------------------

The BIOS Parameter Block (BPB) determines the nature of a disk medium.
It can be found in the DOS boot sector of every formated disk.  This DOS
boot sector is at track 0, head 0, sector 1, on diskettes, and follows
the primitive boot sector and extended disk drive partition table on
hard drives.

A pointer to the memory image of the BPB is passed to a block device
when requesting initialization of the device.  A drive parameter block
can be built with device driver request using the BPB and with the
undocumented function 53h, Int 21h.  See Disk Parameter Block.

BIOS Parameter Block Structure:

 Offset  Data type Description

  00H    WORD      Sector size in bytes (not less than 32)
  02H    BYTE      Sectors/Clusters [Allocation Unit](power of 2)
  03H    WORD      Number of reserved sectors (starting at logical sector 0)
  05H    BYTE      Number of FATs (usually 2)
  06H    WORD      Number of directory entries (maximum allowed)
  08H    WORD      Total number of sectors in logical image, including boot
  0AH    BYTE      Media descriptor 11111xxxB (ID byte)
  0BH    WORD      Number of sectors per FAT
  0DH    WORD      Sectors/track
  0FH    WORD      Number of Heads
  11H    DWORD     Number of Hidden Sectors (used in partitioning schemes)
  15H    DWORD     Number of logical sectors if +08H = 0  (DOS 4.0)

DOS 4.0 Boot Sector Extension (created by FORMAT and LABEL commands):

  19H    BYTE      Physical drive number
  1AH    BYTE      Reserved
  1BH    BYTE      Segment byte 29h
  1CH    DWORD     Volume serial number (computed from date/time)
  20H    11 BYTES  Volume Label
  2BH     8 BYTES  Reserved



Example BIOS parameters for drives:

   Diskette:
                  Bytes/  Sec/   Track/ Sides  Bytes  Sec/   Sec/  Sec/  ID
                  Sector  Track   Side                Cluster DIR  FAT  Byte
                 .-------+------+------+-----+-------+------+-----+----+----.
  8.00 inch disk |  128  |  26  |  77  |  1  | 250K  |  4   | 17  |  6 | FE |
                 |  128  |  26  |  77  |  1  | 250K  |  4   | 26  |  6 | FD |
                 | 1024  |   8  |  77  |  2  | 1.23M |  1   |  6  |  1 | FE |
  5.25-inch disk |  512  |   8  |  40  |  1  | 160K  |  1   |  4  |  1 | FE |
                 |  512  |   8  |  40  |  2  | 320K  |  2   |  7  |  1 | FF |
                 |  512  |   9  |  40  |  1  | 180K  |  1   |  4  |  2 | FC |
                 |  512  |   9  |  40  |  2  | 360K  |  2   |  7  |  2 | FD |
                 |  512  |  15  |  80  |  2  | 1.20M |  1   | 14  |  7 | F9 |
  3.50-inch disk |  512  |   9  |  80  |  2  | 720K  |  2   |  7  |  3 | F9 |
                 |  512  |  18  |  80  |  2  | 1.44M |  1   | 14  |  9 | F0 |
                 `-------+------+------+-----+-------+------+-----+----+----'

  Hard Disk:
                  Bytes/  Sec/   Cylin. Heads  Bytes  Sec/   Sec/  Sec/  ID
                  Sector  Cylin.                      Cluster DIR  FAT  Byte
                 .-------+------+------+-----+-------+------+-----+----+----.
  XT 10 Mb 5.25" |  512  |  17  |  306 |  4  | 10Mb  |   8  |  32 |  8 | F8 |
  AT 20 Mb 5.25" |  512  |  17  |  615 |  4  | 21Mb  |   4  |  32 | 40 | F8 |
  PS/2 20 Mb 3.5"|  512  |      |      |     | 21Mb  |      |     |    | F8 |
  PS/2 44 Mb 3.5"|  512  |  17  | 1022 |  5  | 44Mb  |  17  |  32 | 43 | F8 |
  PS/2 70 Mb 3.5"|  512  |      |      |     | 70Mb  |      |     |    | F8 |
                 `-------+------+------+-----+-------+------+-----+----+----'

-----------------------------------------------------------------------------
System ROM Parameter Table:
-----------------------------------------------------------------------------

Function 0C0h under Int 15h returns a pointer to this table in ES:BX.

 Offset Data type  Description

  00H   WORD       byte_count  number of bytes following (min.=8)
  02H   BYTE       model       PC XT PCjr AT PS/50/60 XT/2 PS/30 CVT PS/80
                               FF FE FD   FC          FB   FA    F9  F8
  03H   BYTE       submodel                     04 05 01   00    00  00
  04H   BYTE       BIOS_rev    0 for first release, 1 for 2nd, etc.
  05H   BYTE       featbyte   80 = DMA channel 3 used by hd BIOS
                              40 = 2nd 8259 installed
                              20 = Real-Time Clock installed
                              10 = Int 15h, AH=41h called upon Int 9 (keyboard
                                   scan code hook)
                               8 = wait for external event supported
                                   (Int 15h, AH=41h) (CVT); reserved on PS/2
                               4 = extended BIOS area allocated at 640K
                               2 = bus is Micro Channel instead of PC
                               1 = reserved
  06H   WORD       0  reserved
  08H   WORD       0  reserved

----------------------------------------------------------------------------
CPU Global Descriptor Table:
-----------------------------------------------------------------------------

The global descriptor tables are used to perform block moves in  the
protected mode of the 80286/386 with Int 15h, function 87h, and for
switching to virtual mode, function 89h.

GDT organization:

     offset 0  null descriptor
            8  GDT descriptor
           10  IDT descriptor
           18  DS
           20  ES
           28  SS
           30  CS
           38  uninitialized, used to build descriptor for BIOS CS

Sample descriptor:

SOURCE_TARGET_DEF   STRUC

SEG_LIMIT      DW     ?   ; Segment limit (1 to 65536)
LO_WORD        DW     ?   ; 24-bit segment physical address (0 to 16M-1)
HI_BYTE        DB     ?   ;
DATA_ACC_RIGHT DW    93H  ; Access rights byte (CPL0-R/W)
Reserved       DW     0   ; Reserved word (must be 0)

SOURCE_TARGET_DEF   ENDS

Global descriptor table pointed to by ES:SI in Int 15h, function 87h:

BLOCKMOV_GDT_DEF    STRUC
               DW     0,0,0,0  ; First dummy descriptor
CGDT_LOC       DW     ?,?,?,0  ; Location of calling routine GDT
SOURCE         DW     ?,?,?,0  ; Source descriptor - segment to be moved
TARGET         DW     ?,?,?,0  ; Target descriptor - destination segment
BIOS_CS        DW     ?,?,?,0  ; BIOS code descriptor - protected mode CS
TEMP_SS        DW     ?,?,?,0  ; Stack descriptor - protected mode SS
BLOCKMOV_GDT_DEF    ENDS

_____________________________________________________________________________
-----------------------------------------------------------------------------
BIOS Video Structures:
-----------------------------------------------------------------------------
Screen Attribute Byte:
-----------------------------------------------------------------------------

In alphanumeric modes (0-3 and 7), character data is stored in Map 0,
character attributes in Map 1, and character patterns in Map 2.  Map 0
and Map 1 can be viewed as a single buffer, with a character/attribute
pair stored at even addresses.

  Bit  Function

   7   Monochrome blinking or color background Intensity
   6   Red background
   5   Green background
   4   Blue background
   3   Foreground intensity or character select (see Char. Map Select Reg.)
   2   Red foreground
   1   Green foreground
   0   Blue foreground

Mixed colors:   Non-intense:               Intense:
                                         No color      = Grey
              Green + Blue  = Cyan       Green + Blue  = Light Cyan
              Red   + Blue  = Magenta    Red   + Blue  = Light Magenta
              Red   + Green = Brown      Red   + Green = Yellow
                                         All three     = High intensity white
-----------------------------------------------------------------------------
Screen Dynamic Video State Table:
-----------------------------------------------------------------------------

This table is returned in a 64K byte buffer using Int 10h, function 1Bh,
'Get Video BIOS Functionality/State Information'.

 Offset  Data type  Description

  00H    DWORD     Address of static video functionality table
  04H    BYTE      Video mode
  05H    WORD      Number of displayed character columns
  07H    WORD      Length of displayed portion of video buffer in bytes
  09H    WORD      Start address of upper left corner of video buffer
  0BH    16 BYTES  Table of cursor locations (col.,row) for 8 video pages
  1BH    BYTE      Cursor end line
  1CH    BYTE      Cursor start line
  1DH    BYTE      Active video page
  1EH    WORD      I/O port for CRTC address register
  20H    BYTE      CRT_MODE_SET (current value of 3x8H register)
  21H    BYTE      CRT_PALETTE (current value of 3x9H register)
  22H    BYTE      Number of displayed character rows
  23H    WORD      POINTS (height of displayed character matrix)
  25H    BYTE      Active display combination code
  26H    BYTE      Inactive display combination code
  27H    WORD      Number of displayed colors (0 for monochrome)
  29H    BYTE      Number of video pages supported
  2AH    BYTE      Raster scan lines: 0=200,1=350,2=400,3=480
  2BH    BYTE      Alphanumeric character table used when
                    attribute bit 3 is 0 (VGA) 0=Block0,...0FFh=Block255
  2CH    BYTE      Alphanumeric character table used when
                    attribute bit 3 is 1 (VGA) 0=Block0,...0FFh=Block255

  2DH    BYTE      Misc. state information (1 if true):
                    Bit 0= all modes active on all video subsytems
                        1= gray-scale summing enabled
                        2= monochrome display attached
                        3= default palette loading disabled
                        4= cursor emulation enabled
                        5= blinking attribute enabled
                        6=7 reserved
  2EH    BYTE      reserved
  30H    BYTE      reserved
  31H    BYTE      Video RAM available: 0=64K,1=128K,2=192K,3=256K
  32H    BYTE      Save area status (1 if true):
                    Bit 0= two alphanumeric char. sets active (VGA)
                        1= dynamic save area is active
                        2= alphanumeric char.set override is active
                        3= graphics char.set override is active
                        4= palette override is active
                        5= display combination code extension active
                        6-7 reserved
  33H-33FH         Reserved

----------------------------------------------------------------------------
Screen Static Video Functionality Table:
-----------------------------------------------------------------------------

The address for this table appears as the first double word in the
dynamic video state table.  The dynamic video table is returned in a 64K
byte buffer using Int 10h, function 1Bh, 'Get Video BIOS
Functionality/State Information'.

 Offset Data type  Description

  00H    BYTE      Video modes supported (1 if supported)
                    Bits 0-7=modes 0-7
  01H    BYTE      Video modes supported
                    Bits 0-7=modes 8-15
  02H    BYTE      Video modes supported
                    Bits 0-3=modes 16-19; bits 4-7 reserved
 03-06H  4 BYTES   Reserved
  07H    BYTE      Scan lines available in alphanumeric mode (1 if avail.)
                    Bit 0=200,1=350,2=400 lines
  08H    BYTE      Maximum number of displayable alphanumeric char.sets
  09H    BYTE      Number of available alphanumeric character definition
                    tables in char. generator ROM
  0AH    BYTE      Misc. video BIOS capabilities (1 if available)
                    Bit 0= all modes on all monitors (0 for MCGA)
                        1= Gray-scale summing
                        2= char.set loading
                        3= default palette loading
                        4= cursor emulation
                        5= 64-color palette
                        6= video DAC loading
                        7= control of video DAC via attrib. controller
                            color select
  0BH    BYTE      Misc. video BIOS capabilities (1 if available)
                    Bit 0= light pen support
                        1= save/restore video state
                        2= blinking/background intensity
                        3= display combination code
                       4-7 reserved
  0CH    BYTE      Reserved
  0DH    BYTE      Reserved

  0EH    BYTE      Save area capabilities
                    Bit 0= multiple alphanumeric char.sets
                        1= dynamic save area
                        2= alphanumeric char.set override
                        3= graphics character set override
                        4= palette override
                        5= Display Combination Code extension
                       6-7 reserved
  0FH    BYTE      Reserved
----------------------------------------------------------------------------
Screen Alphanumeric Character Pattern Table:
-----------------------------------------------------------------------------

The alphanumeric character pattern table addressis stored in the Int 1Fh
vector.

This is a pointer to graphic characters to replace 80H-FFH (8x8 matrix
read from top to bottom to make 8 bytes per character). Used in color
graphics mode.

_____________________________________________________________________________
-----------------------------------------------------------------------------
MS-DOS Structures:
----------------------------------------------------------------------------
Disk Parameter Block (DPB):
-----------------------------------------------------------------------------

The disk parameter block is an internal parameter block used by MS-DOS,
and is built from the BIOS Parameter Block (BPB).  Function 32h under
Int 21h can be used to locate the disk parameter block.  A different
disk parameter block can be generated for each unit of a block device
driver, supporting different media.

The DOS disk partition length limitation of 32 Megabytes comes from the
fact that MS-DOS uses WORD storage for logical sector pointers.  Each
sector is nominally 512 bytes.  This limitation is shown in DOS
interrupt functions Int 25h and Int 26h.

Internal Disk Parameter Block (built by MS-DOS from BPB)

 Offset  Data type Description

  00H    BYTE      Drive Index (0='A', etc.)
  01H    BYTE      Unit code: unit number in device driver
  02H    WORD      Number of bytes/sector
  04H    BYTE      Sectors/cluster - 1
  05H    BYTE      Log base 2 of sectors/cluster
  06H    WORD      Reserved sectors
  08H    BYTE      Number of FAT copies
  09H    WORD      Number of root DIR entries
  0BH    WORD      Sectors in reserve, FATs, and DIR: First data sector
  0DH    WORD      Max number of clusters + 1 available above DIR
  0FH    BYTE      Sectors per FAT (WORD in DOS 4.x, shifting remaining
                   addresses below by one byte.)
  10H    WORD      Sectors in reserve and FATs: First DIR sector
  12H    DWORD     Pointer to device driver for this device
  16H    BYTE      Media descriptor byte (Disk ID byte)
  17H    BYTE      Validity byte: 0FFH means block must be rebuilt
  18H    DWORD     Address of next device driver or -1 if last
  1CH    WORD      Starting cluster of current directory (0 for root)
                   (DOS 2.x) or cluster to start search for next free
                   cluster (DOS 3.x and 4.x)
  1EH    64 BYTES  ASCIZ string for current directory path (DOS 2.x)
                   or 0FFFFH (DOS 3.x)

----------------------------------------------------------------------------
File Allocation Table (FAT) Structure:
-----------------------------------------------------------------------------


12-bit FAT layout (for DOS 1.x, 2.x, and 3.x if partition is less than
16 Megabytes, i.e. total clusters is less than 4087):

 Tribble Data type Description (values in hex)
 Offset
   0     TRIBBLE   Disk ID byte + F00
   1     TRIBBLE   Filler = FFF
   2     TRIBBLE   Cluster Value:  000 = unused
                               001-FEF = next cluster number
                               FF0-FF6 = reserved cluster
                                   FF7 = cluster marked bad
                               FF8-FFF = last cluster in file
  003H   TRIBBLE   Etc.

16-bit FAT layout (for DOS 3.x if partition is greater or equal to
16 Megabytes, i.e. total clusters is 4087 or greater):
  Word   Data type Description (values in hex)
 Offset
   0     WORD      Disk ID byte + FF00
   1     WORD      Filler = FFFF
   2     WORD      Cluster Value:   0000 = unused
                               0001-FFEF = next cluster number
                               FFF0-FFF6 = reserved cluster
                                    FFF7 = cluster marked bad
                               FFF8-FFFF = last cluster in file

For example, the first file disk directory entry might have a starting
cluster of 0002.  At entry 2 in the FAT, there may be a next cluster
value of 0003; at 3 there may be 0008; at 8 one might find FFF8,
indicating this indexed position is the last cluster in the file.

----------------------------------------------------------------------------
Disk Directory Entry: (See also FCB)
-----------------------------------------------------------------------------

Every formated disk has a root directory where information about files
and subdirectories is kept.  The root directory begins just after the
file allocation tables.  Its starting sectory on the disk can be found
from the BIOS parameter block on the disk's boot sector.  Subdirectories
are stored on disk just like files, with their own cluster assignments.
The first two file structures in a subdirectory have a dot and a double
dot in the filename field, representing the current directory and the
parent directory.

 Offset  Data type Description

  00H    BYTE      First character of filename, or
                   E5H  if file has been erased, or
                   00H  if directory entry has not been used (there
                        are no more used entries in directory), or
                   05H  if first character of file is to be 0E5H, or
                   2EH = '.' if this entry is an alias for the current
                        or parent directory.  If next byte is a space (20H),
                        the cluster field gives the starting cluster for
                        the current directory.  If the next byte is also a
                        dot (2EH), then cluster field has the starting
                        cluster of the parent or zero if the parent is the
                        root directory.
  01H    10 BYTES  The next 7 characters of the filename and the
                     file extension.  Filled with 20H = ' '.
  0BH    BYTE      File attribute:
                     Bit 7-6 Reserved
                          5  Archive (set whenever file is changed)
                          4  Subdirectory
                          3  Volume label (only in root directory)
                          2  System file
                          1  Hidden file
                          0  Read only (file writes denied)
  0CH    10 BYTES  Reserved
  16H    WORD      Time created or last updated
                     Bit 15-11  Binary number of hours (0-23)
                         10- 5  Binary number of minutes (0-59)
                          4- 0  Binary number of even seconds (0-29)
  18H    WORD      Date created or last updated
                     Bit 15- 9  Binary number of years since 1980
                          8- 5  Binary number of months (1-12)
                          4- 0  Binary number of days (1-31)
  1AH    WORD      Starting cluster
  1CH    DWORD     File size

-----------------------------------------------------------------------------
Disk File Control Block (FCB): (See also Disk Directory Entry)
-----------------------------------------------------------------------------

The file control block is a storage buffer for transferring information
about a current file to and from the disk operating system.  Before the
introduction of file handles (i.e. before DOS 2.x), the user was
required to set up his own FCBs for each file accessed.  The structure
of a FCB is:

 Offset  Data type Description

 -07H    BYTE      0FFH = Extended FCB flag indicating seven extra bytes
 -06H    5 BYTES   Reserved
 -01H    BYTE      Attribute of file:
                   Bit 5 Archive
                       4 Subdirectory
                       3 Volume Label
                       2 System file
                       1 Hidden file
                       0 Read-only file
  00H    BYTE      Drive identification: 0=default, 1='A', etc.
  01H    8 BYTES   Filename              space filled.
  09H    3 BYTES   File Extension        space filled.
  0CH    WORD      Current block         (1 block = 128 records)
  0EH    WORD      Record size           (default = 80H = 128 bytes)
  10H    DWORD     File size
  14H    WORD      Date created/updated  (8 bit:year-1980, 5 bit month, day)
  16H    WORD      Time created/updated  (5 bit hour, 6 bit min, even secs)
  18H    8 BYTES   Reserved              (contains device driver pointer)
  20H    BYTE      Current record        Offset of record in block
----------------------------------------------------------------------------
Country Information Table:
-----------------------------------------------------------------------------
The country information table location can be found by using function
38h, Int 21h.

  Country Information Table

 Offset  Data type Description

  00H    WORD      date format (see above)
  02H    5 BYTES   ASCIIZ string showing currency country symbol
  07H    2 BYTES   ASCIIZ string showing thousands separator character
  09H    2 BYTES   ASCIIZ string showing decimal separator character
  0BH    2 BYTES   ASCIIZ string showing date separator character
  0DH    2 BYTES   ASCIIZ string showing time separator char
  0FH    BYTE      currency format
                   bit 1 = number of spaces between value and currency symb.
                   bit 0 = 0 if currency symbol precedes value
                           1 if currency symbol follows value
  10H    BYTE     Number of digits after decimal in currency
  11H    BYTE     Time format
                   bit 0 = 0 if 12-hour clock
                           1 if 24-hour clock
  12H    DWORD    Address of case map routine (FAR CALL) for codes >7Fh
                   Call with AL=ASCII code to be converted, AL=return.
  16H    BYTE     Data-list separator char
  17H    BYTE     Null = 00H
  18H    10 BYTES  reserved

 Time and Date format:
  0 = USA standard    h:m:s m/d/y
  1 = Europe standard h:m:s d/m/y
  2 = Japan standard  h:m:s y:m:d

----------------------------------------------------------------------------
Device Driver Device Information Word:
-----------------------------------------------------------------------------

The device information word is passed to a device driver through Int
21h, function 44h (IOCTL).  Its setting is very similar to the third
word in the device driver header.

  Bits  15  = 0  reserved
        14  = 1  if can handle control codes
       13-8 = 0  reserved
        7   = 1  character device
            = 0  block device
        6   = 1  EOF on input
     Character Device:                  Block Device:
        5   = 1  'raw' mode               Bits 5-0 = drive index
            = 0  'cooked' mode                       (0='A', 1='B', etc.)
        4   = 0  reserved
        3   = 1   clock
        2   = 1   null device
        1   = 1   console output device
        0   = 1   console input device
----------------------------------------------------------------------------
Device Driver Header:
-----------------------------------------------------------------------------

The device driver header appears as the first block of data in a device
driver.  Device drivers are installed by the operating system, starting
with the NUL device driver.  MS-DOS contains default device drivers for
the console (CON:), a logical printer (PRN:), an auxiliary device
(AUX:), serial devices (COMx:), parallel devices (LPTx:), and a system
clock (`CLOCK).  Replacement or supplemental drivers can be added using
device driver file names in the CONFIG.SYS file.  Note that a device
drive file name may not be the name needed to refer to the device in a
device open call.  The device name appears at offset +0AH in the device
driver header.

Offset  Data type  Description

  00H    DWORD     Pointer to next device or -1
  04H    WORD      attribute:
               bit: 15 = 1 if character device, 0 if block device
                    14 = 1 if IOCTL (can handle control strings)
                    13 = if block device, 1 = non-IBM format
                         if char. device, 1 = supports output-until-busy
                    12 = 0 reserved
                    11 = 1 if device supports OPEN/CLOSE/REMOVABLE
                  7-10 = 0 reserved
                     6 if supports Get/Set Logical Device
                     5 if char. device, 1='raw' mode, 0='cooked' mode
                     4 if char. device, 1=Special
                     3 if char. device, 1=Current CLOCK$
                     2 if char. device, 1=Current NUL Device
                     1 if char. device, 1=Current Standard Output
                     0 if char. device, 1=Current Standard Input
  06H    WORD      pointer to strategy entry
  08H    WORD      pointer to interrupt entry
  0AH    8 BYTES   If char. device, name field
                   If block device, 1 byte unit number

Communication with device drivers is usually performed by the operating
system through request packets.

----------------------------------------------------------------------------
Device Driver Device Request Header and Device Request Packet:
-----------------------------------------------------------------------------

The device request header is used by the operating system to communicate
with a particular device driver.  It forms the beginning of the device
request packet, a memory structure described below:

Offset in device request header:
For all functions:
         + 0  byte length
         + 1  byte unit code ('minor' device index)
         + 2  byte command code

Extended Offset for device request packet:
function 0 init :
         + D byte number of units
         + E dword break addr
         +12 dword BPB array
function 1 media chk :
         + D byte media desc. from BPB
         + E byte returned
function 2 build BPB :
         + D byte media desc. from BPB
         + E dword transfer addr. (128 bytes) or FAT
         +12 dword BPB
function 3,12 IOCTL in out, 4 read, 8,9 write, with verify
         + D byte media desc. from BPB
         + E dword transfer addr
         +12 word byte/sector count
         +14 word starting sector number
function 5 non-dest. read
         + D byte read from device
function 6 in status, 10 output status
function 7 input flush, 11 output flush
         + 3  word status (0 on entry)
             bit 15=1=>ERROR in bits 7-0
             bit  9=1 device not busy on status call
             bit  8=1 device operation complete
         + 5  Dword to ms-dos queue
         + 9  Dword to device queue

----------------------------------------------------------------------------
Memory Control Block:
-----------------------------------------------------------------------------

The memory control block is a 16 byte prefix to all programs and each
copy of the environment.  It is used by the operating system to keep
track of memory allocation, and can be found 16 bytes below the Program
Segment Prefix.  The first MCB can be found using function 52h of Int
21h.

 Memory Control Block structure:

 Offset  Data type Description

  00H    BYTE      4DH if in chain, 5AH if end of chain ('MZ'=Mark Zbikowski)
  01H    WORD      0 if free or Program owner PSP segment word
  03H    WORD      size (in paragraphs) of controlled memory arena


----------------------------------------------------------------------------
Environment Block:
-----------------------------------------------------------------------------

The environment blocks reside in memory just before each child process,
unless they have been deallocated by a resident program.  The original
environment is located just after the COMMAND processor.  It can be
found by using function 52h of Int 21h to get the first memory control
block, then jumping through the MCBs to locate the desired environment
block.

The environment blocks contain the definitions of variables used by DOS
and by application programs.  For example, COMSPEC, used in the
CONFIG.SYS file, and PATH and PROMPT, used in the AUTOEXEC.BAT file, are
entered into the original environment as variables.  Moreover, the SET
command defines user variables in the environment.

Environment Block Structure:

 Offset  Data type Description

  00H    n1 BYTES  ASCIIZ string in form: 'PARAMETER1=VALUE1',0
  n1+1   n2 BYTES  ASCIIZ string in form: 'PARAMETER2=VALUE2',0
   etc.
  nz     BYTE      0  end of variable definition strings
  nz+1   WORD      Count of number of following ASCIIZ strings (DOS 3.xx)
  nz+3   ns BYTES  Name of Current Process as ASCIIZ string (DOS 3.xx)

Note that variable definitions end with a double null.  The current
process ASCIIZ string contains the path and filename for the program
residing in memory which owns the environment block.  This information
was not available before DOS 3.xx.


----------------------------------------------------------------------------
Program Segment Prefix:
-----------------------------------------------------------------------------

Before any program is run, MS-DOS sets up a 256 byte program segment
prefix containing termination vectors, default file control blocks, and
the tail of the command line used to start the program.  (This structure
is a carry-over from the CP/M operating system.)  The file control
blocks are filled in with one or two file names if these are found in
the correct format in the command line tail.

PSP Structure:

 Offset  Data type Description

  00H  WORD        INT 20H
  02H  WORD        end of allocation block segment (top of memory)
  04H  2 BYTES     reserved
  06H  WORD        number of bytes available in this segment
  08H  2 BYTES     reserved
  0AH  DWORD       contents of INT 22H termination vector
  0EH  DWORD       contents of INT 23H ^C break vector
  12H  DWORD       contents of INT 24H critical error vector
  16H  WORD        parent PSP segment
  18H  BYTE        open files (0FFH=unused)
  19H  19 BYTES    reserved
  2CH  WORD        segment of environment block
  2EH  DWORD       old stack address
  32H  BYTE        maximum open files
  34H  DWORD       old file address
  36H  25 BYTES    reserved
  50H  WORD        long call address to DOS INT 21H handler
  5CH  16 BYTES    default FCB #1
  6CH  16 BYTES    default FCB #2
  80H  128 BYTES   command tail and default DTA

----------------------------------------------------------------------------
DOS Driver List:
-----------------------------------------------------------------------------

The DOS drive list is reference data for device drivers kept in memory
by  the operating system. It is an undocumented internal data area which
is strongly version dependent. A pointer to this list is returned by the
internal function 52h under Int 21h.

 Offset  Data type Description

  00H    DWORD     Pointer to first disk parameter block
                   (each disk parameter block contains pointer to next one)
  04H    DWORD     Pointer to internal data area
  08H    DWORD     Pointer to CLOCK$ device driver
  0CH    DWORD     Pointer to actual CON: device driver

If DOS 2.x:

  10H    BYTE      Number of logical drives in system
  11H    WORD      Maximum bytes/block of any block device (512)
  13H    DWORD     Pointer to current internal disk transfer area
  17H    n BYTES   Beginning of NUL device driver.

If DOS 3.x:

  10H    WORD      Maximum bytes/block of any block device (0200h)
  12H    DWORD     Pointer to current internal disk transfer area
  16H    DWORD     Pointer to drive dynamic information array:

Drive Dynamic Information Array (81 bytes per drive, starting
with drive A:
     00H  69 BYTES Current path as ASCIIZ string, starting with 'x:\'
     45H  DWORD    Pointer to disk parameter block for this drive
     49H  WORD     Reserved
     4BH  DWORD    Reserved
     4FH  DWORD    Reserved

 1AH     DWORD     Pointer to data area
 1EH     WORD      Reserved
 20H     BYTE      Number of block devices
 21H     BYTE      Value of LASTDRIVE command in CONFIG.SYS (default 5)
 22H     n BYTES   Beginning of NUL device driver.

-----------------------------------------------------------------------------
Font Files and Code Pages Images:
-----------------------------------------------------------------------------

Code page images are contained in font files (extension .CPI). These can
be downloaded to the device, if the device has a code page switching device
driver entry in CONFIG.SYS.

 Data type  Value  Description

file_header:

  8 BYTES   ?      0FFH,"font   "  Font tag (7 characters)
  8 BYTES   0      Reserved
  WORD      1      Number of pointers in header (1 for DOS 3.3)
  WORD      1      Type of info pointer (1 in DOS 3.3)
  2 WORDS   ?      Offset info, 0  Displacement of info in file

info:

  WORD      1      Number of code page entries

code_page_header:

  WORD      ?      Size of this code page header
  2 WORDS   0,0    Pointer to header of next code page
  WORD      1      Device type: 1 = display, 2 = printer
  8 BYTES   ?      "EGA     "  Device sub type ID
  WORD      ?      999  Code page ID
  3 WORDS   0      Reserved

data_header:

  WORD      1      Reserved (must be 1)
  WORD      ?      Number of fonts
  WORD      ?      Length of following font data


If the font file is for a display device, then:

font_1:

  BYTE      ?      character size, rows
  BYTE      ?      character size, columns
  2 BYTES   0,0    aspect ratio
  WORD      256    number of characters
  ...
                   pixel description for all 256 characters
  ...
font_2:
  ...
font_3:
  ...
Else, if font file is for a printer, then:

selection_type_1:

  WORD      1      selection type (1=4201, 2=5202 Proprinter)
  WORD     12      total number of bytes in control sequences
  6 BYTES   5,27,"I",0,27,"6" defines hardware code page
  6 BYTES   5,27,"I",4,27,"6" defines downloadable code
  ...              character description of download

selection_type_2:

  WORD      2      selection type
  WORD     12      total number of bytes in control sequences
  6 BYTES   27,"[","T",5,0,0,0,1,181,0,26,"6"  select active page 437
  ...              character description of download

_____________________________________________________________________________
-----------------------------------------------------------------------------
DOS File Formats:
-----------------------------------------------------------------------------
File EXE Program Header:
-----------------------------------------------------------------------------

All .EXE files on disk begin with a header to determine how the segment
and pointer registers are to be initialized, and to relocate absolute
addresses.

EXE header and program structure:

 Offset  Data type Description

  00H    BYTE      4DH signature byte 1
  01H    BYTE      5AH signature byte 2 (for Mark Zbikowski)
  02H    WORD      file size modulo 512
  04H    WORD      file size in pages, including header
  06H    WORD      number of relocatable table items
  08H    WORD      size of header in paragraphs
  0AH    WORD      Min. number of paragraphs needed above program
  0CH    WORD      Max. number of paragraphs desired above program
  0EH    WORD      segment displacement of stack module
  10H    WORD      contents of SP at entry
  12H    WORD      word checksum
  14H    WORD      contents of IP register at entry
  16H    WORD      segment of displacement of code module
  18H    WORD      offset of first relocation item in file
  1AH    WORD      overlay number (0 for resident part of program)
  1CH    n BYTES   reserved space
                   relocation table
                   reserved space
                   program and data segments
                   stack segment

-----------------------------------------------------------------------------
MicroSoft Object Module Structure:
-----------------------------------------------------------------------------

Object modules are files created by language compilers as an intermediate
step between source code and machine code.  Individually, they have
a .OBJ extension to their name.  Collectively, in libraries, they have
a .LIB extension.

Each object module contains a sequence of variable-length records.
Each record has the following format:

  1 BYTE  Record Type (80H to 0B0H)
  1 WORD  Record Length (for next n+1)
  n BYTES Record Body
  1 BYTE  Checksum (Sum of all n+4 bytes = 0 mod 256)

Record Types:

  (Index Fields coded as: Actual length if < 128 size
        81H , 2-byte size
        84H , 3-byte size
        88H , 4-byte size)

  80H THEADR Translator Header Record (always first record of .obj file)
      The record body, the T-module name, is a variable-length field
      containing:
      1 BYTE  The length of the name of the object module
      n BYTES The name of the object module defined by NAME in MASM

  88H COMENT Comment Record (never between FIXUPP and LEDATA or LIDATA)
      Record body:
      1 BYTE  Attribute: Bit 7=1 No Purge: Utilities should preserve comment.
                             6=1 No List:  Utilities should not list comment.
                             5-0 0
      1 BYTE Comment Class: 0   Language-translator name given by comment.
                            1   Copyright given by comment.
                            2-9BH Reserved by Intel
                            9CH MS-DOS version number.
                            9DH Memory model: s,c,m,l, and h for
                                   small, compact, medium, large, and huge
                            9EH Sets Microsoft LINK's DOSSEG switch.
                            9FH Default library search name.
                            A1H Microsoft extensions to Intel object
                                   record specifications are used.
                            C0H-FFH Reserved.
      n BYTES Comment Field

  8AH MODEND Module End Record (Always last record in .obj file)
      Record body:
      1 BYTE Module type: Bit 7=1 if module is a main program
                              6=1 if if this record contains a START address
                              6-1 0
                              0=1 START address is relocatable (always
                                     for 8086 code)
      n BYTES START address field (when Module type bit 6=1)
              Format: EndDat, FrameDat, TargetDat, TargetDispl.
                      (See FIXUPP record for interpretation.)

  8CH EXTDEF External Names Definition Record
      Record body:
      1 BYTE  Name Length (n= 0-7FH)
      n BYTES External Name
      1 BYTE  Type index: TYPDEF record index associated with External Name
              (unless 0).

  8EH TYPDEF Type Definition Record (Precedes EXTDEF or PUBDEF records which
             reference a TYPDEF)
      Record body:
      1 BYTE  Name field (0 for Microsoft TYPDEF)
      n BYTES Intel Eight-Leaf Descriptor field (Microsoft uses only four)
              1 BYTE  0
              m BYTES Leaf Descriptor: Four Fields ("Leaves") to describe
                      the type and size of a variable:
                      1 BYTE  Variable Type
                            = 62H if NEAR Variable
                            = 61H if FAR  Variable
                      1 BYTE  Variable Subtype (ignored by LINK)
                            = 77H Array
                              79H Structure (NEAR variable only)
                              7BH Scalar (NEAR variable only)
                      i BYTES Size of communal variable (if NEAR) or
                              Number of elements of array (if FAR)
                              as an Index Field
                      t BYTES For FAR array only: Index of previous
                              NEAR TYPDEF containing the array data
                              type and size of elements in array;
                              Index of 1 means first TYPDEF, etc.


  90H PUBDEF Public Names Definition Record (must be after GRPDEF and SEGDEF
             records to which it refers; PUBDEF usually placed near end of
             object module).
      Record Body:
      n BYTES Public Base
              i BYTES Group Index Field references a previous GRPDEF record
                      (0 means no group associated with this PUBDEF)
              i BYTES Segment Index Field references a previous SEGDEF record
                      (if 0, Frame Number used and Group Index = 0)
              1 WORD  Frame Number (only if GI and SI = 0). Specifies
                      the start of an absolute segment.  Value indicates
                      the number of the frame containing the public name.

      m BYTES Public Name
              1 BYTE  Length of name (< 128)
              p BYTES Name
      1 WORD  Public Offset of location referred to by Public
              Name.  Offset assumed to lie within segment, group,
              or frame specified in the public base field.
      i BYTES Type Index
              Index Field references a previous TYPDEF.
      ...
      Above three fields can be repeated to declare a list of public names.

  94H LINNUM Line Number Record relates line numbers in source to
             addresses in object code. (Must be after SEGDEF to which
             they refer.  LINNUM records generally placed near end
             of object module).
      Record body:
      l BYTES Line Number Base
              1 BYTE  Group Index = 0
              i BYTES Segment Index. Index Field references previous
                      SEGDEF record.

      1 WORD  Line Number (0 to 32,767)
      1 WORD  Line Number Offset in executable code in segment specified
              in the Line Number Base field to which the line number in
              the Line Number field refers.
      ...
      Above two fields can be repeated, so that a single LINNUM record
      can specify multiple line numbers in the same segment.

  96H LNAMES List of Names Record.  List of names that can be referenced
      by subsequent SEGDEF and GRPDEF records.  LNAMES records usually
      placed near start of object module.
      Record Body:
      n BYTES Name List
              1 BYTE  Length of name (0-255)
              l BYTES Name
              ... up to 255 logical names, implicitly index 1,2,...


  98H SEGDEF Segment Definition Record describes a logical segment in an
      object module, giving the segment's name, length, alignment, and
      the way the segment can be combined with other logical segments.
      LINK limits the number of SEGDEFs to 255 per object module.
      Record body:
      n BYTES Segment Attributes
              1 BYTE  ACBP byte:
                Bits 7-5  Alignment in the run-time memory map
                        = 0 A = Absolute
                        = 1 Relocatable, byte (1) aligned
                        = 1 Relocatable, word (2) aligned
                        = 1 Relocatable, paragraph (16) aligned
                        = 1 Relocatable, page (256) aligned
                     4-2  C = Combination with other segments
                        = 0 if A = 0 or private segment
                        = 1 not used by Microsoft
                        = 2 can be concatenated with another segment
                            with the same name; used with 'public'
                            combine type
                        = 3 undefined
                        = 4 same as C = 2 for Microsoft
                        = 5 can be concatenated with another segment
                            with the same name; used with 'stack'
                            combine type
                        = 6 can be overlapped with another segment
                            with the same name; used with 'common'
                            combine type
                        = 7 save as C = 2 for Microsoft
                       1  B = Big
                        = 1 (and Segment Length = 0) only if the
                            segment is exactly 64K long
                       0  P = Page-resident (not used in MS-DOS)
                        = 0 for Microsoft
              x BYTES Frame Number and Offset (present only for
                      A = 0 in ACBP byte)
                      1 WORD  Frame Number for start of segment
                      1 BYTE  Offset (0-0FH) Ignored by LINK
        1 WORD  Segment Length in bytes (0-0FFFFH).  If segment is
                exactly 64K, Segment Length = 0 and B = 1 in ACBP.
        i BYTES Segment Name Index Field identifies the segment
                with a unique name.
        i BYTES Class Name Index Field identifies the segment with a
                class name (such as CODE, FAR_DATA, or STACK).  The
                linker places segments with the save class name into
                a contiguous area of memory in the run-time memory
                map.
        i BYTES Overlay Name Index Field identifies the segment with a
                run-time overlay.  Ignored by LINK ver. 2.40 and later.

  9AH GRPDEF Group Definition Record defines a group of segments, all
      of which lie within the same 64K frame in the run-time memory map.
      LINK limits number of GRPDEF to 21.
      Record body:
      i BYTES Group Name Index Field indicates the name in LNAMES record.

      n BYTES Group Component Descriptor
              1 BYTE  Type = 0FFH means following field is Segment Index.
              i BYTES Segment Index Field identifies previous SEGDEF record.
      ...
      Group Component Descriptor is usually be repeated.


  9CH FIXUPP Fixup Record contains information to allow linker to
      resole addresses.  FIXUPP records describe the location of
      each address value to be fixed up, the target address to
      which the fixup refers, and the frame relative to which the
      address computation is performed.  FIXUPP must immedately
      follow LEDATA or LIDATA record if it refers to one of these.
      Record body:
      n BYTES Thread Field. FIXUPP may contain 0 or more Thread Fields.
              Format:
              1 BYTE  Thread Data
                  Bits 7   = 0 Start of thread field
                       6   = 1 if thread specifies a frame
                             0 if thread specifies a target
                       5   = 0 unused
                       4-2 = Method:
                          Frame specified by:
                             0 a segment index
                             1 a group index
                             2 an external index
                             3 explicit frame number (not supported by LINK)
                             4 the segment in which the Location is defined;
                               the largest possible frame number is used.
                             5 the Target's segment, group, or external index.
                          Target specified by:
                             0 a segment index and a displacement.
                               The displacement is given in the Target
                               Displacement field of the FIXUPP record.
                             1 a group index and a Target Displacement.
                             2 an external index and a Target Displacement.
                               LINK adds the displacement to the address it
                               determines from the external name's corresponding
                               PUBDEF record in another object module.
                             3 an explicit frame number (not supported by LINK).
                             4 a segment index alone (displacement = 0)
                             5 a group index alone
                             6 an external index.  The Target is the address
                               associated with the external name.
                             7 an explicit frame number (not supported by LINK).
                       1-0 = Thread Number (0-3) for Frame or Target. The
                             thread number can be reused in an object module;
                             if so, it refers to the thread field in which
                             it last appeared.
        i BYTES Thread Index Field:
                If Method = 0 : Segment index in previous SEGDEF record
                            1 : Group index in previous GRPDEF record
                            2 : External index in previous EXTDEF record
                            3 : Explicit Frame number (not supported by
                                LINK; ignored)

      n BYTES Fixup Field; provides information needed to resolve a
              reference to a relocatable or external address.  FIXUPP may
              contain 0 or more Fixup Fields.
              Format:
              1 WORD Locat field:
                      Bits:    7    = 1  indicates fixup field
                               6    = M = 1 if fixup is segment relative
                                          0 if fixup is self-relative
                               5    = S = 0 unused
                             4-2    = Loc field for type of Location to fix:
                                      0 = Low-order byte
                                      1 = Offset
                                      2 = Segment
                                      3 = Pointer (Segment:offset)
                                      4 = High-order byte (not recognized
                                          by LINK)
                                      5 = Loder-resolved offset (treated
                                          as Loc=1 by LINK)
                           1-0,15-8 Data Record Offset; indicates the
                                    position of the Location to be fixed
                                    in LEDATA or LIDATA immediately preceding
                                    the FIXUPP record.  This offset indicates
                                    either a byte in the Data field of an
                                    LEDATA record or a data byte in the Content
                                    field of an Iterated Data Block in an
                                    LIDATA record.
              1 BYTE  Fix Dat:
                      Bit   7  = F = 1 if Frame for this fixup is specified
                                     by reference to a previous Thread Field;
                                   = 0 if the Frame method is explicitly
                                     defined in this fixup field.
                           6-4 = Frame:
                                 If F=1, Frame = number (0-3) of thread field
                                         containing the Frame method;
                                    F=0, Frame = Thread Field Method number
                                         (0-5)
                             3 = T = 1 if Target for fixup is specified by
                                       a reference to a previous Thread field
                                     0 if the Target is explicitly defined in
                                       this fixup field
                             2 = P bit; determined by 1-0 bits:
                           1-0 = Targt field: If T=1, Targt contains the
                                 number of the previous Thread field containing
                                 the Target method and P bit combined with
                                 the 2 low-order bits of the Method field in
                                 the Thread field determines the Target method;
                                 If T=0, target is explicitly defined and the
                                 P and Targt fields contain number (0-6) of
                                 one of the Target fixup methods under the
                                 Thread Field method bits for Target.
              i BYTES Frame Datum is an index field that refers to a previous
                      SEGDEF, GRPDEF, or EXTDEF record, depending on the
                      Frame method.
              i BYTES Target Datum contains a segment index, a group index,
                      or an external index field depending on the Target
                      method.
              1 WORD  Target Displacement present only if the P bit in
                      the Fixdat field is 0.  If so, Target Displacement
                      contains the offset used in methods 0-2 specifing
                      a Target.


  A0H LEDATA Logical Enumerated Data Record
      The LEDATA record contains contiguous binary data, executable code
      or program data, that is eventually copied into the program's
      executable binary image.
      Record body:
      i BYTES Segment Index Field refers to a previous SEGDEF to which
              data is to be placed.
  A2H LIDATA Logically Iterated Data Record
      The LIDATA record contains binary data (code or program data)
      which can be specified by a repeating pattern rather than by
      explicit enumeration.
      Record body:
      i BYTES Segment Index Field refers to previous SEGDEF to which
              data is to be placed.
      1 WORD  Iterated Data Offset into the segment referenced by the
              Segment Index; relative to the base of the segment;
              determines where the enumerated data will be placed in
              the run-time memory map.
      d BYTES Iterated Data Block (may be nested to contain one or
              more other iterated data blocks):
              1 WORD  Repeat Count for contents field
              1 WORD  Block Count for number of iterated data blocks
                      in content field
              n BYTES Content: Either nested iterated data blocks
                      if the Block Count is nonzero, or data; if
                      data:
                      1 BYTE  Number of data bytes in field
                      m BYTES Actual data
  B0H COMDEF Communal Names Definition Record
      The COMDEF record is a MicroSoft extension to the basic set
      of Intel record types; recognized by LINK 3.50 and later.
      Record body (can be repeated):
      c BYTES Communal Name
              1 BYTE  Length of name
              n BYTES Name
      i BYTES Type Index Field references a previous TYPDEF record
              in the object module, or 0 if no public name associated.
      1 BYTE  Data Segment Type
              = 61H  FAR
                62H  NEAR
      n BYTES Communal Length indicates the amount of memory to be
              allocated for the communal variable.
               If Data Segment Type is NEAR, the Communal Length
                  contains the size (in bytes) of the communal variable;
               If Data Segment Type is FAR, the Communal Length Field is:
                  i BYTES Number of Elements (Index Field) in communal
                          variable array of elements
                  i BYTES Element Size (Index Field) for each element
                          in the comunal variable array.
-----------------------------------------------------------------------------