1. AN INTRODUCTION TO TROUBLESHOOTING

Troubleshooting is usually to easy; vaned symptoms appear depending on 
points of failure.  This section decribes two procedures which may allow
easier troubleshooting and subsequent repair:
1. Check-out procedure
   Objective: To guide the user through a problem isolation process when
              symptoms do not indicate a specific component malfunction.
   Fault isolation level: Repair by ;unit replacement, repair can be 
                          accomplished with a basic knowledge of computer
                          hardware.
2. Unit repair flowchart
   Object: To guide the user through a component level repair process.
   Allow component-level repair of an individual faulty unit.
   Fault isolation level: Component level- Requires an advance knowledge
   of computer hardware engineering, and electronic.

General troubleshooting procedure
* First, isolate and replace the faulty unit according to the check-out
  procedure, each time a unit is replaced, to make sure the new unit is
  not faulty.  This procedure will prevent confusion with a problem
  caused by a poor connector contacts.

* Second, isolate and replace the faulty component in the unit according
  to the unit flowchart or the troubleshooting table.

              Step 1                    Step 2
         ----------------          ----------------
         (  Check-out   )   ---\   (  Unit repair )
         (  procedure   )   ---/   (   flowchart  )
         ----------------          ----------------
          Repair by unit            repair at com-
           replacement               ponent level

     NOTE 1) All checks indicated on the flowchart must be made.
             Should any unit or component be replaced disregarding
             any check, the newly installed one might be damaged.
     NOTE 2) Whenever you are lost in the repair procedure, return
             to the entry and restart the procedure.
     NOTE 3) When no exit is found, during a diagnostic procedure 
             (e.g., the test procedure has resulted in repeating a 
             diagnostic loop), proceed with the repair according
             to the trouble table.


2. TEST PROGRAM
The test program provides tests for the ten functions listed in 
Table 1.  It allows either one of the following two execution modes:
* AUTO Mode
  In this mode, the program automatically performs a six test cycle. 
  If desired, the cycle may be repeated up to 99 times.  The number
  of cycles may be selected after loading the program.  This mode is
  suitable for an aging test after repair or a test on a problem of
  very low reproducibility.

* MANUAL Mode
  The manual mode allows the user to select any one test from those
listed in Table 1 and is an aid to component troubleshooting.



                                   1






              Table 1: Functions tested by the program
              ----------------------------------------
                No.    Tested Function
              ----------------------------------------
                 1     RAM CHECK
                 2     BUZZER CHECK
                 3     RS,SER CHECK
                 4     LCD CHECK
                 5     MCMT CHECK
                 6     DIP-SW READ CHECK
                 7     KEY BOARD CHECK
                 8     ANALOG INPUT CHECK
                 9     BARCODE CHECK
                10     CLOCK CHECK

2.1 REPAIRING TOOLS
Table 2, lists necessary repair tools which are available from EPSON.

              Table 2: REPAIR TOOLS                               QTY
              -------------------------------------------------------
                1      Test program                                1
                2      RS-232C interface mini-wrapping connector   1
                3      Serial interface mini-wrapping connector    1 
                4      Microcassette tape                          1
                5      Cable assembly (P/N B778400201)             1
                6      DC regulator or dry-cell battery            1
                7      Low-resolution barcode reader               1

2.3 LOADING THE TEST PROGRAM
Set the POWER switch ON and load the program.
After the above preparation, the following menu will appear on the LCD
pannel.
          ---------------------------------------------------
          |  TEST PROGRAM MENU MODE Ver 1.0                 |
          |                                                 |
          |      1 : AUTO                                   |
          |      2 : MANUAL                                 |
          ---------------------------------------------------


2.4 SELECTING A TEST MODE
In the responce to the menu, key in "1" or "2", respectively, to select
the AUTO or MANUAL test mode.
* AUTO mode
  When the AUTO mode is selected ("1" is keyed in), the prompt:
          ---------------------------------------------------
          |  CHECK COUNT ?                                  |
          ---------------------------------------------------
  should appear.  Specify a number of test cycles to be run by 
  responding with a number from 1 to 99.  RAM, buzzer, RS-232C
  interface, serial interface, LCD unit, microcassette tape drive 
  and DIP switche test make up one test cycle.  When the AUTO mode
  is selected, this cycle is repeated according to the number of times
  specified in the response to the prompt.





                                   2







* MANUAL Mode
          ---------------------------------------------------
          |  TEST PROGRAM SELECT                            |
          |   1.RAM CHECK           2.BUZZER CHECK          |
          |   3.RS,SER CHECK        4.LCD CHECK             |
          |   5.MCMT CHECK          6.DIP-SW READ CHECK     |
          |   7.KEY BOARD CHECK     8.ANALOG INPUT CHECK    |
          |   9.BARCODE CHECK      10.CLOCK CHECK           |
          ---------------------------------------------------
   Select a test by keying in the number preceding the test.  When the
   test is completed, the display stops.  To repeat the test again,
   press the apace bar, otherwise, press the RETURN key.  To stop the
   test after the keyboard check has been selected, key in "Break".
   * If any error message appears, refer to section 2.6

2.5 TEST RUN PROCEDURE AND DISPLAY INFORMATION
This section describes the procedure for running the individual tests
and display information given by them.
          ----------------------------------------------
          |                                            |
          |  MEMORY & V-RAM CHECK                      |
          |                                            |
          ----------------------------------------------

   (1) RAM Check
       The RAM and V-RAM check tests are performed in succession and
       the following messages are displayed when the tests are 
       completed.
          ----------------------------------------------
          |  RAM CHECK END !!                          |
          |  VRAM CHECKING !!                          |
          |  VRAM CHECK END NOW !!                     |
          ----------------------------------------------

  (2) Buzzer Check
      * The buzzer sounds for approximately three seconds.
      * The buzzer further sounds at two different tones and then the
        following is displayed:
          ----------------------------------------------
          |  BUZZER OK ?                               |
          ----------------------------------------------
      * Adjust the sound level and do another check.

  (3) RS-232C and Serial Interface Check
      Step 1: Insert the RS-232C interface and the serial interface
              connectors, which are connected according:
                Serial interface       RS-232C interface
                ----------------       -----------------
                 4 shorted to 5         6 shorted to 7
                 2 shorted to 3         2 shorted to 3
                                        4 shorted to 5 shorted to 8
              (The sockets are labeled on the PX-8 case.)






                                   3







      Step 2: Key in "3" for the test menu (TEST PROGRAM SELECT).  The
              RS-232C and the Serial Interface Check will be selected.
              The program runs the RS-232C interface test first, 
              displaying the following information:
          ---------------------------------------------------
          |  RS232C CHECKING                                |
          |  RS232C CHECK END NOW                           |
          ---------------------------------------------------
      Step 3: The program then runs the serial interface test and 
              display the following information:
          ---------------------------------------------------
          |  HIGH SPEED SERIALING                           |
          |  HIGH SPEED SERIAL END NOW !!                   |
          ---------------------------------------------------
      Step 4: These messages indicate the end ot the test.

  (4) LCD Check
      * The entire LCD panel display is reversed.
      * The LCD panel dispaly is reversed every other dot and then the
        black and white conbination is reversed.
      * The LCD panel display is reversed every four dots and then the 
        black and white conbination is reversed.
      * The following character pattern appears, and the test ends.
          ---------------------------------------------------
          |       *****  CHRAGENE TEST                      |
          | !"#$%&'()*+,-./0123456789:;<=>?@ABC...XYZ...    |
          ---------------------------------------------------

  (5) MCMT (Microcassette Tape Drive)
      * The following prompt appears:
          ---------------------------------------------------
          |  SPEAKER ON ? (Y/N)                             |
          ---------------------------------------------------
        If speaker sound output is desired, depress "Y" (YES); if not,
        press "N" (NO), and the next prompt will appear as follows:
          ---------------------------------------------------
          |  IS THIS TAPE INITIALIZE ? (Y/N)                |
          ---------------------------------------------------
        Examine the tape and respond with "Y" to this prompt if the
        tape data may be destroyed.  Otherwise, key in "N".
      * A Rewind/Fast Feed and Read/Write check test are performed
        after the following information message is displayed:
          ---------------------------------------------------
          | MCMT CHECK (REWIND, F.F & READ/WRITE CHECK)     |
          ---------------------------------------------------
      * The third prompt appears as follows:
          ---------------------------------------------------
          | WRITE TAPE INFORMATION TO THIS TAPE ? (Y/N)     |
          ---------------------------------------------------
      * The test ends with the following information message:
          ---------------------------------------------------
          | WRITE DATA & STOP                               |
          | HEAD OFF                                        |
          ---------------------------------------------------







                                   4





  (6) DIP SW Read Check
      The following information is displayed:
           ------------------------
           |           87654321   | DIP switch SW4 elements 1 - 8
           |   INITIAL=00101111   | Element setting
           |           00101111   |
           ------------------------

      * Make sure that the DIP switcj setting agrees with the following
        table.
                          DIP Switch Settings
          -------------------------------------------------
          | Character set specification | 1 2 3 4 5 6 7 8 |
          |-----------------------------|-----------------|
          | ASCII (USA)                 | 1 1 1 1 0 1 0 0 |
          | French                      | 0 1 1 1 0 1 0 0 |
          | German                      | 1 0 1 1 0 1 0 0 |
          | English                     | 0 0 1 1 0 1 0 0 |
          | Danish                      | 0 1 0 1 0 1 0 0 |
          | Swedish                     | 0 1 0 1 0 1 0 0 |
          | Norwegian                   | 0 1 1 0 0 1 0 0 |
          | Italian                     | 1 0 0 1 0 1 0 0 |
          | Spanish                     | 0 0 0 1 0 1 0 0 |
          | HASCI                       | 0 0 0 0 0 1 1 0 |
          | Japanese(Japanese language) | 1 0 0 0 0 1 0 0 |
          | Japanese(kana)              | 0 0 0 0 0 0 0 0 |
          | Japanese(touch 16)          | 1 0 0 0 0 0 0 0 |
          -------------------------------------------------

  (7) KEYBOARD CHECK
      Step 1: Select your keyboard type by responding with the number
              following the specification of your unit.
              The following display prompt will appear:
           --------------------------------------------------
           | THEN DSP DATA KEY-IN !!                        |
           --------------------------------------------------

      Step 2: In responce to the above prompt, key in characters to be 
              displayed in the following order:
         1- ESC   13- 1     25- 7     37-       49- F     61- ;     
         2- PAUSE 14- TAB   26- Y     38-       50- C     62- .
         3- HELP  15- 2     27- 8     39- BS    51- G     63- :
         4- PF1   16- Q     28- U     40-       52- V     64- / 
         5- PF2   17- 3     29- 9     41-       53- H     65- RETURN
         6- F3    18- W     30- I     42- CTRL  54- B     66- SHIFT
         7- PF4   19- 4     31- 0     43- A     55- J     67  \
         8- PF5   20- E     32- O     44- SHIFT 56- N     68- GRAFT
         9-  [    21- 5     33- -     45- S     57- K     69- CAPS LOCK
        10-  ]    22- R     34- P     46- Z     58- M     70- SPACE
        11- INS   23- 6     35- ^     47- D     59- L     71- CTRL
        12- DEL   24- T     36- @     48- X     60- ,

        When the key data entry ends, the following prompt appears.
           --------------------------------------------------
           |  ONCE MORE KEY-BOARD CHECK ? (Y/N)             |
           --------------------------------------------------



                                   5

 




  Step 3: If the keyboard check, part 2, test is desired, respond with
          "N" to this prompt.  Otherwise, key in "Y".  The above part 1 
          test will be repeated.
  * The program enters the part 2 test and displays the following 
    prompt:
          ---------------------------------------------------
          |  KEY-BOARD CHECK Part 2                         |   
          |          PUSH KEY-IN !!                         |
          ---------------------------------------------------

    Step 4: Key in the same characters as randomly displayed, following
            the above prompt.

    Step 5: To terminate the test, key in "break".  The program will
            end the test leaving the following information message:
          ---------------------------------------------------
          |  KEY-BOARD CKECK Part 2 END !!                  |
          ---------------------------------------------------

(8) Analog Input Check
    Step 1: Connect a DC voltage regulator (output voltage range should
            be from 0v to +2.0v) and a dry-cell battery.  Use the cable
            assembly P/N B778400201 acccording to the instructions in 
            section 2.5 - 3.
    * The program displays the connected voltage at an accuracy of 0.02v.

    Step 2: When a DC voltage regulator is used, compare the displayed 
            value with the reading.  If a dry-cell battery is used, 
            measure and cmpare its voltage.

(9) Barcode Check
    * The following is displayed:
          ---------------------------------------------------
          |  INPUT                                          |
          ---------------------------------------------------
    Step 1: Read the barcde pattern using a reader.
    * If the pattern and read data agree, "OK" appears on the LCD panel.

(10) Clock Check
     * The following prompt appears:
          ---------------------------------------------------
          |  TIME SET ? (Y/N)                               |
          ---------------------------------------------------
     Step 1: If you would like to set the time, respond with "Y" to 
             this prompt; otherwise, key in "N".
     *When "Y" is keyed in above, the time setting guide message is 
     displayed:
          ----------------------------------------------------------
          |  INPUT DATA  Year/ Month/ Day/ Hour: Minute: Sec/ Week |
          |  Week Data Code                                        |
          |       Sun:00 Mon:01 Tue:02 Wed:03 Thu:04 Fri:05 Sat:06 |
          ----------------------------------------------------------

    Step 2: Key in the date and time as follows:
            year,month,day,week,day,hour,minute, and seconds.
    * The set time should be updated every one second.






                                   6






2.6 TEST PROGRAM MESSAGES
The test program displays a message on the LCD panel when it terminates
normally.  When any malfunction is found, a diagnostic code indicates
the problem area.
Major error messages are explained in the following:

(1) Return codes from slave CPU6303
          ---------------------------------------------------
          |  EPSP ERROR !!  XX                              |
          ---------------------------------------------------
    The slave CPU operation being performed when an error occurs is
    indicated on the LCD panel as a one-byte "XX" return code.  The
    following table lists all the available return codes and summarizes
    their meanings.

Device   Code                Meaning
----------------------------------------------------------------------
 SYS   |  00  |  Normal processing termination
 SYS   |  01  |  Break ACK:
       |      |    Indicates that a break took place.
 SYS   |  02  |  Command error:
       |      |    Indicates that a command has been input which is
       |      |    not included in the defined system.
 SYS   |  03  |  Communication error:
       |      |    Indicates that a command is received when data
       |      |    was to be received/sent or vise versa.
 2CD   |  11  |  Illegal size:
       |      |    Indicates that a screen-over occured which is 
       |      |    attributable to an illegal size specification.
 2CD   |  12  |  An undefined graphic character was used.
 2CD   |  13  |  An alphabetic character code was used. Or, an
       |      |    attempt was made to define any other than that
       |      |    for alphabetic character.
 MCT   |  41  |  Head error:
       |      |    Indicates that the head failed to operate normally.
 MCT   |  42  |  The tape stopped during processing.
 MCT   |  43  |  Write protect error:
       |      |    An attempt was made to write a tape with no 
       |      |    write protect pin.
 MCT   |  44  |  Data error:
       |      |    Indicates that the data could not be determined
       |      |    to be either 1 or 0 because the data pulse is 
       |      |    wider or narrower that the standard value.
 MCT   |  45  |  CRC error.
 MCT   |  46  |  Block mode error:
       |      |    A block whose identifer is other that that 
       |      |    specified.
 ESPS  |  61  |  A linkage failed.
 ESPS  |  62  |  Communication error:
       |      |    Overrun or framing error.
 ESPS  |  63  |  Timer over.
 BEEP  |  71  |  Beep already in progress:
       |      |    Indicates that a BEEP or MELODY was attempted when
       |      |    another BEEP or MELODY was already in progress.
----------------------------------------------------------------------



                                   7






(2) Ram error message:
          ---------------------------------------------------
          |  ERROR !! ADDRESS ****H                         | 
          |            WRITE DATA  **H READ DATA  **H       |
          ---------------------------------------------------
    D-RAM compare error - Written and read-back data did not agree.

          ---------------------------------------------------
          |  ERROR !!  BEFORE ADDRESS  ****H                |
          |              SAVE DATA  ** READ DATA   **H      |
          ---------------------------------------------------
    D-RAM compare error - The RAM test was attempted on a program
                          area (including OS, TPA, and RAM files) 
                          no read/write test is allowed.

          ---------------------------------------------------
          |  VRAM ERROR ADDRESS  ****H                      |
          |           WRITE  **H READ  **H                  |
          ---------------------------------------------------
    V-RAM compare error - Written and read-back data did not agree,

(3) RS-232C and Serial Interface error message
          ---------------------------------------------------
          |  RS232C CHECK TIME OUT !!                       |
          ---------------------------------------------------
    RS-232C transmission/reception failure- DIR > DSR, 
           RTS > CTS > CD, TXD > RXD.

          ---------------------------------------------------
          |  RS232C ERROR TRNSMIT  ****H RECIVE  ****H      |
          ---------------------------------------------------
    RS-232C transmitted/received data failed to agree.

          ---------------------------------------------------
          |  ERROR CODE **                                  |
          ---------------------------------------------------
    RS-232C error XX occured:  08-Parity error
                               10-Overrun error
                               20-Framing error

          ---------------------------------------------------
          |  HIGH SPEED SERIAL I/O ERROR !!                 |
          |       TRANSMIT DATA  ****H RECIVE DATA  **** H  |
          ---------------------------------------------------
    Data transmitted/received via the serial interface failed to agree.

(5) MICROCASSETTE error messages
          ---------------------------------------------------
          |  MCMT INITIALIZE (READ ERROR) TIME UP !!        |
          ---------------------------------------------------
    Microcassette tape initialization failure - possibly a machanical
    fault.




                                   8






          ---------------------------------------------------
          |  MCMT WIND &F.F. TEST CHECK COUNT  ****         |
          |                      RESULT COUNT  ****         |
          ---------------------------------------------------
    Tape count (photo-reflector output) error during rewind/fast feed.

          ---------------------------------------------------
          |  MCMT READ/WRITE CHECK HEAD ERROR  !!           |
          ---------------------------------------------------
    Read/write head loading/unloading failure.

          ---------------------------------------------------
          |  MCMT READ/WRITE CHECK TAPE STOP ERROR  !!      |
          ---------------------------------------------------
    Tape feed failure during read/write - the reel stops rotating.
   
          ---------------------------------------------------
          |  MCMT READ/WRITE CHECK ERROR  !!                |
          |   RDC ERROR !! CORE  **                         |
          ---------------------------------------------------
    Read/write error - possibly an abnormal tape feed speed or improper
                       read/write pulse width.

          ---------------------------------------------------
          |  MCMT READ/WRITE CHECK READ ERROR  !!           |
          |  READ  **     WRITE E5                          |
          |  BLOCK COUNT  ****  TO  ****                    |
          ---------------------------------------------------
    Compare error - written and read-back data failed to agree.

          ---------------------------------------------------
          |  THIS TAPE CAN'T WRITE                          |
          |    CHANGE ANOTHER TAPE  !!                      |
          ---------------------------------------------------
    Write failure.

          ---------------------------------------------------
          |  LET'S CHANGE THE MC-TAPE                       |
          ---------------------------------------------------
    Read failure.

          ---------------------------------------------------
          |  ONCE MORE KEY-IN !!                            |
          |  KEY-CODE ERROR  !!                             |
          ---------------------------------------------------
    Key entry code mismatch - a key code other than the specified one
                              was input.  Up to five key entry retrials
                              are allowed.

(6) Barcode error message
          ---------------------------------------------------
          |  FOUND  *****                                   |
          |  BARCODE ERROR CHECK ERROR                      |
          |  TRY ONCE MORE  !!                              |
          ---------------------------------------------------
    Barcode pattern read failure.



                                   9






3. UNIT LEVEL TROUBLESHOOTING
When trouble-shooting a faulty unit, first find the entry routine for
that unit from the entry table.  In such a case where there are more
that one symptom is observed and symptoms vary during the course of
troubleshooting, make it a practice to enter troubleshooting procedures
according to the symptom that occurred first.

Notes on using the flowcharts:
1) The troubleshooting flowcharts do not necessarily include all 
   information required for troubleshooting such as check modes,etc.
   Thus, the flowchart context and trouble symptoms should be closely
   examined.
2) I troubleshooting flowchart instructions lead you into a loop or
   to the end of a procedure and the problem is not resolved, refer 
   to the schematic drawings or procedeed by troubleshooting according
   to the following procedure.

Step 1: Replace the faulty unit with a good one and make sure that the
        faulty unit is really malfunctioning.
Step 2: If the problem is difficult to reproduce or occurs so briefly
        that it is hard to examine the symptom, vary the supply voltage 
        according to the following instructions.
        (a) Disconnect the battery from the battery connector CN2.
        (b) Prepare a variable (0-10)DC voltage regulator and make sure
            that the output is turnrd off.
        (c) Connect the regulator to the CN2 connector in place of the 
            battery.
        (d) Adjust the regulator output voltage to +5V.
        (e) Turn the regulator output on.

After the above setup is completed, vary the regulator output in a range
from 4.8V to 6.0V and examine the unit operation at each voltage level.
If this voltage margin test is successful, maintain the voltage and
proceed with troubleshooting, using the check-out procedure and
troubleshootng flowchart.
     






















                                  10