WORDSTAR CONFIGURATION FOR OKIDATA MICROLINE 80/82A/83A/84/92/93 
              PRINTERS AND THE OSBORNE EXECUTIVE I

NOTE: This file comes from Stephen Hill in Cupertino, Calif.
      As I do not have an Okidata printer, I cannot directly check
      the instructions, but they should be useful to those of you
      who do have Oki printers.
                                Jim Switz, FOG Executive Librarian
                                           26 December 1983

     This information for Okidata Microline-series printer 
installation comes from a factory bulletin dated August 15, 1983.
If you have any questions or problems after consulting your 
computer manuals, contact your dealer or

                     Technical Support Group
                       OKIDATA Corporation
                        111 Gaither Drive
                     Mt. Laurel, N. J. 08054
           609-235-2600   (ask for Technical Support)

     The configuration is accomplished first by running the SETUP 
program (ref. pp. 75-81, vol. 1, Executive Guide).  
     Place the CP/M disk in drive A.
     Place the Wordstar disk in drive B.
     Type SETUP (CR) after the A> prompt.
     Screen 1 appears: "Select source for configuration"
          Select:  From Drive B
     Screen 2: "Select the items you want to change"
          Select:  Key definitions (CR)
          Move curser to "Arrow Settings", then (CR)
     Screen 3:  "Select standard arrow key definition"
          Move curser to "Wordstar Standard", then (CR)
          Press (ESC) key to return to Screen 2.
     Press (ESC) key again.
     Screen 2.  Move curser to "Printer Port", then (CR)   
          Configuration is:
          Baud rate = 1200
          Protocol  = no protocol
          Device Selection = Other (AUXIN:/AUXOUT:)
          Initialization String = none

          Move curser to "Parallel Port", then (CR)
          Configuration is:
          Protocol = Centronics
          Device Selection = Printer (LST:)
          Initialization String = <ESC>1  (Note: press Escape 
          key, release it, press 1 key, release it, then press 
               (CTRL)(CR)
     Move curser to:  "Exit to Save Menu", then (CR)
     Save Setup to: Drive B

     Important note:  All of the above SETUP configurations 
should be saved on your CP/M and SuperCalc disks, EXCEPT, under 
Parallel Port, the Initialization String = none.  The <ESC>1 
string instructs the printer to print in correspondence mode.

     A menu-driven program named INSTALL, included on the 
Wordstar package, is the second program to run.  This program 
allows you to tell Wordstar what kind of printer you are using 
and how it operates.  (References:  vol. 2, pp. 176-189 Executive 
Guide, and Nov. 1983 FOGHORN, p. 32).

     Wordstar operates many of the same functions as the 
Microline Printer, including boldface, double strike, 
underscoring, and other word processing features.  

     Insert Wordstar INSTALL in Drive A.
     Insert Wordstar disk in Drive B.
     Boot the system.
     Answer the questions upon prompt.
     You will then get to the Installation Menu.

     Select "C" Menu of Printers  
          Select either "standard printer" or "Okidata ML84A" (if 
          you have this model).                    
          Communications Protocol = "A" none
          Driver = "A" operating system primary list device.
     Select "D" Custom Installation of Printer
          A menu will appear.

        Select "F" Boldfacing (^PB)

          The patches are as follows:

          80        82A/83A        84/92/93
          --        -------        --------
          03        no patch           03
          
        Select "I" Ribbon Selection (^PY)

          The patches are entered as hexadecimal.  Precede each           
          number with a comma.  Press (CR) after each number. Eg.           
          ,03 (CR)
          "Alternate Ribbon Selection - first ^PY"
          This patch toggles between underlining and not           
          underlining.

          80        82A/83A        84/92/93
          --        -------        --------
          no patch  no patch            02
                                        1B             
                                        43
                                        (CR)
          "Stardard Ribbon Selection - second ^PY"

          80        82A/83A        84/92/93
          --        ------         --------
          no patch  no patch            02
                                        1B
                                        44        
                                        (CR)
        Select "J" Vertical Motion (^PT and ^PV)

          "Start Vertical Motion - ^PT" (superscript)

          80        82A/83A        84/92/93
          --        ------         --------
          no patch  no patch            02
                                        1B
                                        4A   
                                        (CR)
          "Stop Vertical Motion - ^PV" (subscript)

          80        82A/83A        84/92/93
          --        ------         --------
          no patch  no patch            02
                                        1B
                                        4C
                                        (CR)
          VMI minimum value = -1
          VMI range value   = -2
          Line Feed Function Code = (empty)
          Reverse Line Feed Function Code = (empty)
          
        Select "O" User Defined Function

               "User function #1"   (^PQ)

          80        82A/83A        84/92/93    Mode
          --        ------         --------    ----
          01        01             01        80       = 16.5 cpi
          1D        1D             1C        82A/83A  = 16.5 cpi
          (CR)      (CR)           (CR)      84/92/93 = 12 cpi
          (CR)      (CR)           (CR)

               "User function #2"   (^PW)

          01        01             01        80       = 5 cpi
          1F        1F             1F        82A/83A  = 5 cpi
          (CR)      (CR)           (CR)      84/92/93 = 5 cpi
          (CR)      (CR)           (CR)

               "User function #3"   (^PE)

          01        02             01        80       = 10 cpi
          1E        1D             1D        82A/83A  = 8.3 cpi
          (CR)      1F             (CR)      84/92/93 = 17 cpi
          (CR)      (CR)           (CR)

               "User function #4"   (^PR) 

          01        01             01        80       = 10 cpi
          1E        1E             1E        82A/83A  = 10 cpi
          0         0              0         84/92/93 = 10 cpi
          (CR)      (CR)           (CR)
          
        Select "Q" Character Pitch

               "Select alternate pitch"   (^PA)

          80        82A/83A        84/92/93
          --        ------         -------
          02        02             02        80       = 8 lpi
          1B        1B             1B        82A/83A  = 8 lpi
          38        38             31        84/92/93 = corresp.
          (CR)      (CR)           (CR)

               "Select standard pitch"   (^PN)

          02        02             02        80       = 6 lpi
          1B        1B             1B        82A/83A  = 6 lpi
          36        36             30        84/92/93 = data 
          (CR)      (CR)           (CR)

     Notes:  1.  If you ML-84 printer is not a Step 2 printer, 
     then the codes for 12 cpi and 17 cpi will be switched.
     2.  Correspondence mode is not supported in 17 cpi on the 
     ML-92 and ML-93.

------------------------

Wordstar (R) is a registered trademark of MicroPro International 
Corporation.