ZCPR3 Z3TCAP (MYTERM.Z3T) file to source code (MYTERM.Z80)
generator.

Program Name:  TCSRC
Author:  Terry Hazen
Version:  1.4
Date:  24 August 90

Version 1.4:  Has a new command line syntax to make it compatible
with ENVSRC.  The RC function is now correctly described in this
document.


Since it is difficult to extensively customize an existing
Z3TCAP.Z3T file by patching alone, TCSRC was written to help the
user customize his Z3TCAP by creating a commented source code
file (MYTERM.Z80) from an existing MYTERM.Z3T file for his
terminal, such as one extracted from Z3TCAP.TCP by TCSEL, or from
the current Z3TCAP located in memory in the ZCPR3 environment.
TCSRC also allows you to create a blank commented Z3TCAP source
code file when you want to start from scratch.  The new source
code file can then be edited as desired, assembled to MYTERM.COM
and renamed to MYTERM.Z3T.  It can then be loaded to your
environment using LDR.COM, NZCOM.COM, JETLDR.COM, etc.

TCSRC generates Z3TCAP commented source code based on the
extended Z3TCAP defined by VLIB4D.  VLIB4D modifies the sequence
of control strings in the extended Z3TCAP over that specified by
earlier VLIB4 beta releases to bring all the terminal control
strings into a common area located prior to the graphics area,
reduces the length of the terminal name to 13 bytes and adds a
byte defining the offset of the graphics area from the start of
the Z3TCAP.

TCSRC expects input files to be subsets of the VLIB4D standard,
such as standard Z3TCAP files.  Consult the current VLIB4 help
files for explanations of each of the defined terminal functions
and consult your terminal manual for information on the terminal
control strings required to implement the terminal functions for
your terminal.

Source code generated by TCSRC from earlier extended Z3TCAP files
with different extended formats will begin to be incorrect when
the sequence of control strings begins to differ from the new
VLIB4D standard and will have to be corrected with a text editor.
Lines of source code defining terminal control strings may simply
be moved into the correct order, ignoring both comments and
labels (except for GOELD, which is used to define the graphics
area offset), as the corrected source code file can be assembled
to a COM file and TCSRC can then be used again to quickly
generate a new, correctly commented source code file.


Syntax
------

     TCSRC [[dir:]infile[.z3t]] [[dir:]outfile[.z80]]

     Default outfile is infile.Z80 on default directory.  Any
     existing R/W file of the same name will be overwritten.

     Infile 'BLANK' creates blank commented source code file.

     If no infile is specified, Z3TCAP.Z80 is created from
     the Z3TCAP in the environment.


The companion utility ENVSRC creates commented source code from
your ZCPR3 environment using the latest extended environment
definitions.


Graphics TCAP Offset
--------------------

VLIB4D defines a graphics offset byte at GOFF (Z3TCAP+12), which
contains the offset from the start of the Z3TCAP to the start of
the graphics area at GEOLD, to allow the future addition of
terminal control strings in the terminal control string area
without requiring rewritting of the VLIB graphics routines using
the graphics data.  To compensate for the addition of the
graphics offset byte, the length of the terminal name area has
been reduced to 13 bytes.


Terminal Configuration Bytes
----------------------------

VLIB4D defines two terminal configuration bytes at B14
(Z3TCAP+14) and B15 (Z3TCAP+15) to allow an application program
access to terminal characteristics not otherwise specified in the
Z3TCAP.  Application programs such as WordStar4 (with Joe Wright's
WSPAT ZCPR3 patch), V and SCAN now have access to information not
only about terminal control strings, but about how users have
configured their terminals.  Users can set configuration bits
indicating, for example, whether or not their terminals are set
to auto-wrap at the end of a line or auto-scroll at the end of a
screen, whether their terminals use ANSI or ASCII control
sequences, and whether they use reverse video or non-reverse
(usually dim) video for their standout mode.  Not all application
aprograms will check the terminal configuration bytes, but their
presence allows the user some control over how application
programs configure his screen display.

SCAN, for example, checks the auto-wrap and auto-scroll bits to
see whether it can put characters in the last display column on
the screen without causing additional blank lines to be inserted
into the display.  If both bits are 0, the last column is
considered safe, and the whole screen can be used for the
display.  If either bit is set, the last column is considered
reserved and the next-to-last column will be the final column
used.  So if your terminal is configured to not automatically
wrap or scroll, you can set the bits accordingly and SCAN will
use the whole screen.  Joe Wright's WSPAT for WordStar4 uses the
configuration bytes in a similar way, along with the set
attribute string to create WS4 display screens.


Screen Display Configuration
----------------------------

When you start looking at how many ways a given terminal can be
configured by a user and how that configuration can affect screen
displays, it quickly becomes clear that a standard Z3TCAP for a
given terminal type is not adequate to convey more than basic
standard information for that terminal.  It may make a difference
to a screen display intensive applications program, for example,
whether a screen is configured as dark letters on a light screen
or light letters on a dark screen and whether reverse video or a
non-reverse video mode, such as dim or bold is used as standout.
For example, if dim is used as standout mode on a dark screen,
spaces in standout mode won't show up, but if reverse video is
used, they will, creating quite a different display.

If the Z3TCAP for a particular terminal specifies dim as the
standout mode, but the user prefers to use bold, reserving dim
for standard mode, but then wishes to exit to a normal video
command line, he must customize his Z3TCAP to use SO (Start
Standout), SE (End Standout), TI (Terminal Initialization) and TE
(Terminal Deinitialization) to set his terminal according to his
preferences.  In this example, SO would set dim, SE would set
normal, TI would set dim, and TE would set normal video.

Still another user of the same terminal type might prefer half
intensity for standout, and would need to customize his Z3TCAP
accordingly.  So many terminal characteristics may be user
configured, in fact, that it is really the user's responsibility
to create a customized Z3TCAP for his system that reflects his
own preferences.  TCSRC attempts to facilitate this process by
providing the user a handy tool to quickly create Z3TCAP source
code files that may be easily edited and used to create his
working customized Z3TCAP.


Extended Z3TCAP Terminal Control Sequences
------------------------------------------

The source code created by TCSRC includes the LD (delete line at
cursor position) and LI (insert line at cursor position)
sequences added in the extended Z3TCAP defined by VLIB4B.
Applications such as WordStar and SCAN can use these control
sequences to produce better displays.

For screen display intensive applications such as WordStar 4.0
patch WSPAT, Joe Wright added a macro to the Z3TCAP and a routine
in VLIB4C to set terminal display attributes.  The source code
created by TCSRC includes the SA (set Attributes) macro and AT
(the attribute string).

The source code created by TCSRC also includes a CD (clear screen
from cursor to end-of-screen) sequence.  While sequence is, in
some cases, a duplication of part of the CL (Home Cursor and
Clear Screen) sequence, it is now available as a separate control
sequence.


Other New VLIB4D Terminal Control Sequences
-------------------------------------------

For use with windowing routines used in pull-down menus, the
extended Z3TCAP includes provisions for a new RC sequence that
returns the current cursor position in HL and a new RL sequence
that reads the entire line up until the cursor position into a
buffer.  Consult V4LIBD.HLP for more information.


Graphics Extensions
-------------------

VLIB4D adds a new standardized character graphics area beginning
at GOELD (graphics on/off delay).  Graphics extensions include
GO/GE (graphics mode on and off), and CDO/GDE (turn the cursor
off and on).


Graphics Characters
-------------------

Graphics characters used by VLIB4D are one-byte characters that
produce lines, intersections and corners as well as full and
hashed blocks.  For terminals without graphics capability, very
good results can be obtained using the characters '-' and '|' for
horizontal (GHL) and vertical (GVL) line characters.  The
characters '*' and '#' can be used for full (GFB) and hashed
(GHB) blocks, the characters '+' or '*' can be used for corners
and the character '+' for intersections.

Use TCSRC to add graphics characters to your own Z3TCAP and try
BOX.COM from VLIB4D for a demonstration of the new line graphics
as used in a box drawing routine.