ZXRIOP
                             V. 1.1

                          Joe Mortensen
                            03/07/92

INTRODUCTION

ZXRIOP ("Z X-Ray") is my attempt to develop an IOP module which 
can be called during program execution in order to examine any 
memory location and alter it on the fly.  I have an old CP/M 
program called XT.COM (XtraTech by Xpert Systems).  It is an RSX 
with functions which go far beyond the limits of ZXR, but one 
which I've found indispensable for program development.  However, 
XT uses a lot of memory and it is not Z-System wise.  If XT is 
loaded, ZDE hangs when you try to exit an editing session.  I've 
hoped that someone else might develop such a useful tool, but so 
far I'm not aware that anyone has.  ZXR requires ZCPR3 or higher 
and a Z-System with a standard 12 record IOP.  The time function 
works only with ZD/ZSDOS and the appropriate clock module.

INSTALLATION

With ZCPR 3.3 and 3.4 ZXR needs no installation.  With ZCPR 3.0 
you must patch the address of your Z3 environment at offset 09h 
in IOPZXR.COM.

LOADING

ZXR is loaded by IOPZXR.  If Z-System is not present or if there 
is no IOP space, it won't load.  To remove IOPZXR type the 
command IOPZXR /R. 

USING ZXR

The trigger key is ^@ (user-configurable with IOPZXR.CFG).  On 
line 24 of the screen this menu appears:

C=Chg  D=Dump  E=Env  T=Time  Q=Quit ?

                   Changing a Byte or Bytes

If you press C, a ? appears asking you for an address in memory.  
ZXR expects up to a four digit hex number as input.  Terminate 
input of less than four digits with RETURN.  BACKSPACE is also 
recognized if you enter a wrong value.  The address is displayed 
and the byte at that location, for example:

EF80 C3 

At this point two actions are possible.  

1.  You can enter a new value (say FF) which is echoed and then 
the next byte is displayed:

EC80 C3 FF 06 

2.  Pressing the space key passes over a byte and displays the 
next.  A maximum of eight bytes can be viewed and changed if 
desired in one change operation.  After the eighth byte is 
handled (or RETURN is pressed), the full line is redisplayed 
along with a menu:  ADQ ?  (A for Another address to change, D 
for Dump -- it will ask for an address, or Q to quit.)

                    Dumping a Memory Location

To display a given line of memory, press D.  The ? prompt 
appears, expecting up to a 4 digit hex number of an address in 
RAM.  Input of less than four digits is terminated with 
RETURN.  BACKSPACE is also recognized to correct a wrong value.  
ZXR then displays the address and 16 bytes in both hex and ASCII.

The dump menu is:  <>ACQ ?  The '<' or ',' key moves back 16 bytes 
and displays one line of bytes.  the '>' or '.' key moves forward 
16 bytes.  The A command asks for a new memory location to 
display.  C allows you to go directly to the change routine.  Q 
returns you to the main memory.

                     Environment Parameters

The E command displays the current system locations:  CCP, BDOS, 
BIOS, ENV, and CBIOS.

                              Time

If you are running ZD/ZSDOS and have a clock and clock module 
loaded, ZXR will display the current date and time.  Pressing any 
key restores the main menu.  ZXR will run without ZD/ZSDOS but 
won't respond to the "Time" command.


NZBLTZ and ZXRIOP

NZBLTZ provides an easy way of having ZXRIOP available.  With 
ZXRIOP loaded in the IOP save the system image with NZBLTZ.  I 
use ZXRIOP mostly when I am testing assembly language programs so 
I have saved the version of NZCOM with it present.  When I run
ASSEM.COM ZXRIOP is already there ready to use.

Please report any bugs or operating problems to me.
Joe Mortensen
4214 Chelsea Ct.
Midland MI 48640
Voice:  517 835-6923
Ladera ZNode: 213 670-9465