====================================
              DOCUMENTATION FOR MORROW MM300 MODEM
              MANUFACTURED BY CTS CORP. (300 BAUD)
              ====================================
              Information supplied by: Ken Cummings
.PAŠLOCAL (OFFLINE) COMMANDS:


    COMMANDS                                 FUNCTION
-------------------------------------------------------------------------

    CTL Q <CR>    TURNS THE MODEM ON AND ENTERS THE LOCAL COMMAND
                  STATE.  BAUD RATE, CHARACTER LENGTH, AND PARITY
                  ARE AUTOMATICALLY DETECTED.

        B <CR>    FROM THE LOCAL COMMAND STATE, THIS COMMAND IS 
                  USED TO RESET THE MODEM INTERFACE CONTROL SOFTWARE 
                  TO THE POWER ON INITIALIZATION POINT.  A CTL Q CR
                  MUST BE USED FROM THIS POINT TO RE-INITIALIZE THE
                  MODEM.  THIS COMMAND IS USED TO CHANGE THE MODEM
                  BAUD RATE.

        R <CR>    FROM THE LOCAL COMMAND STATE,  THIS COMMAND RESETS
                  ALL CONFIGURATION PARAMETERS TO THEIR POWER-ON
                  DEFAULT CONDITION EXCEPT BITS/CHARACTER.

        A <CR>    FROM THE LOCAL COMMAND STATE,  THE MODEM IS PLACED
                  ON-LINE IN THE ANSWER MODE.  AUTOMATIC DISCONNECT
                  IS NOT SUPPORTED IN THIS MODE.

        O <CR>    FROM THE LOCAL COMMAND STATE, THE MODEM IS PLACED
                  ON-LINE IN THE ORIGINATE MODE.  AUTOMATIC 
                  DISCONNECT IS NOT SUPPORTED IN THIS MODE.

        D <CR>    FROM THE LOCAL COMMAND STATE, THIS COMMAND IS USED
                  TO INTERROGATE THE PRESENCE OF A DAIL TONE ON THE
                  TELEPHONE LINE.

        TN <CR>   FROM THE LOCAL COMMAND STATE, THE MODEM WILL TONE
                  DAIL PHONE NUMBER N.

        T <CR>    FROM THE LOCAL COMMAND STATE, THE MODEM WILL TONE
                  DAIL THE PREVIOUSLY STORED NUMBER.

        PN <CR>   FROM THE LOCAL COMMAND STATE, THE MODEM WILL PULSE
                  DAIL THE PHONE NUMBER N.

        P <CR>    FROM THE LOCAL COMMAND STATE, THE MODEM WILL PULSE
                  DAIL THE PREVIOUSLY STORED NUMBER.

                  ADDITIONAL DAIL PARAMETERS.
  
                  A)  THE PHONE CAN BE UP TO 40 CHARACTERS.
                  
                  B)  THE PHONE NUMBER IS AUTOMATICALLY STORED AS LONG
                      AS THE MODEM POWER HAS NOT BEEN SWITCHED OFF.
                      EXECUTING DAIL COMMAND WITHOUT A PHONE NUMBER IN
                      THE COMMAND STRING WILL INVOKE THE STORED PHONE
                      NUMBER.
Š                  C)  "BLANK", "DASH", AND "SLASH" CHARACTERS BETWEEN
                      PHONE NUMBER DIGITS ARE IGNORED.

                  D)  A COMMA CAN BE ENTERED TO CREATE A FOUR SECOND
                      PAUSE BETWEEN DAILING DIGITS.
                      
                  E)  A "W" CHARACTER CAN BE IMBEDDED IN THE PHONE
                      NUMBER TO INSTRUCT THE MODEM DAILER TO WAIT FOR
                      AN INTERMEDIATE DAIL TONE.

                  F)  A "T" OR "P" IMBEDDED IN THE DAIL STRING WILL
                      INSTRUCT THE MODEM TO EITHER TONE OR PULSE DAIL
                      THE DIGITS IN THE STRING.

                  G)  ANY CHARACTER ENTRY AFTER CR AND BEFORE THE
                      REMOTE MODEM HAS ANSWERED WILL HANG UP THE
                      MODEM AND RETURN TO THE LOCAL COMMAND STATE.

                  H)  12 DTMF SIGNALS ARE SUPPORTED BY THE MODEM.
                      THEY ARE 0 TO 9,#,*.

.PA    ŠCN=X<CR>      FROM THE LOCAL COMMAND MODE, THIS SEQUENCE CAN BE
                  USED TO RECONFIGURE VARIOUS CONTROL OPTIONS.

                 N                     FUNCTION
                 ------------------------------------------------------
                 
                 1    NUMBER OF RINGBACKS BEFORE THE LINE IS DISCON-
                      NECTED.  VALUES FOR X RANGE FROM 4 TO F HEX.

                 2    SEND SPACE DISCONNECT OPTION.  WITH THIS OPTION
                      ON, A SPACE TRANSMIT SEQUENCE IS INITIATED UPON
                      DISCONNECT.  THE SPACE SIGNAL TRANSMITS FOR 3.95
                      SECONDS AND THEN RETURNS TO THE LOCAL COMMAND
                      STATE.  X=0, THE SPACE OPTION IS OFF.  X=1, THE
                      SEND SPACE OPTION IS ON.

                 3    9/10 BITS PER CHARACTER LENGTH OPTION.  THIS
                      OPTION IS EFFECTIVE IN BOTH SPEED MODES.
                            
                      9 BPC SELECTION WILL ACCEPT START-STOP CHARACTER
                      WITH ONE START BIT, ONE STOP BIT, AND SEVEN DATA
                      BITS.  (IN THE AUTOMATIC INITIALIZATION MODE,
                      AN ASCII CHARACTER FROM THE INTERFACE WITH NO
                      PARITY OR MARK PARITY WILL ENABLE 9 BPC.)

                      10 BPC SELECTION WILL ACCEPT START-STOP CHARACTER
                      WITH ONE START BIT, ONE STOP BIT, AND EIGHT DATA
                      BITS.  (IN THE AUTOMATIC INITIALIZATION MODE,
                      AND ASCII CHARACTER FROM THE INTERFACE WITH EVEN,
                      ODD, OR SPACE PARITY WILL ENABLE 10 BPC.)
                      X=0, 9 BPC IS SELECTED. X=1,10 BPC IS SELECTED.
                     
                     
                 4    AUTO ANSWER RING COUNTER.  IF X=0, THE AUTO
                      ANSWER MODE IS DISABLED.  IF X=1 TO F HEX, THE
                      MODEM WILL COUNT THE INCOMMING RING SIGNALS AND
                      ANSWER THE PHONE AFTER THE SPECIFIED NUMBER OF
                      RINGS

                 5    BREAK SEQUENCE TIME INTERAVAL PROGRAMMING.  THE
                      TIME INTERVAL IS 200 MS TIMES THE VALUE X.  X 
                      HAS A RANGE OF 1 TO F HEX.

    L <CR>            FROM THE LOCAL COMMAND STATE, THE MODEM CAN BE
                      PLACED IN THE ORIGINATE ANALOG LOOPBACK MODE.
                      ESSENTIALLY, THE MODEM IS IN A NORMAL
                      COMMUNICATION MODE DURING ANALOG LOOPBACK,
                      EXCEPT IT IS NOT CONNECTED TO THE TELEPHONE LINE.
                      ALL ON-LINE COMMAND SEQUENCES ARE SUPPORTED DURING 
                      THE MODE.  THE ON-LINE "E" COMMAND SHOULD BE USED 
                      TO EXIT FROM THIS MODE.

.PAŠON-LINE COMMANDS:

    THE ON-LINE COMMAND STATE PROVIDES A MECHANISM WHERE THE CONTROL
    PARAMETERS OF THE MODEM CAN BE CHANGED WHILE THE PHONE LINE IS STILL 
    CONNECTED TO THE REMOTE MODEM.  ONLY A LIMITED NUMBER ARE SUPPORTED   
    IN THIS MODE.  WHILE THE MODEM IS IN THE ON-LINE COMMAND STATE, DATA
    RECIEVED FROM THE REMOTE MODEM IS LOST.  COMMANDS SENT TO THE MODEM
    WHILE IN THIS STATE ARE TRANSPARENT TO THE REMOTE MODEM.

    TO ENTER THE ON-LINE COMMAND STATE THE INTERFACE MUST ISSUE THE 
    FOLLOWING SEQUENCE:

    CTL T@@@

   AFTER ISSUING THE CTL T@@@ SEQUENCE, THE MODEM WILL SEND THE PROMPT
   "8".  A 50 MS MINIMUM DELAY MUST BE INCORPORATED BETWEEN THE LAST @
   CHARACTER AND THE COMMAND CHARACTER.  AFTER EXECUTING ANY ON-LINE
   COMMAND, THE MODEM WILL RETURN TO THE COMMUNICATION MODE.  IF THE
   MODEM DETECTS A COMMAND ERROR SEQUENCE, THE MODEM WILL ISSUE THE
   PROMPT "E" AND RETURN TO THE COMMUNICATION MODE.   AS AN ADDITIONAL
   NOTE, THE CTL T@@@ SEQUENCE IS PASSED THROUGH THE MODEM TO THE REMOTE   
   STATION.  HOWEVER, THE COMMAND CHARACTER AND CARRIAGE RETURN SEQUENCE  
   IS TRANSPARENT TO THE REMOTE STATION.

   THE FOLLOWING IS A LIST OF ON-LINE CONTROL COMMANDS.

   COMMAND                           FUNCTION
-------------------------------------------------------------------------

    B <CR>    FROM THE ON-LINE COMMAND STATE, THE MODEM WILL SEND A SPACE
              INTERVAL WHICH IS 200MS TIMES THE VALUE STORED IN THE
              CONFIGURATION COMMAND (C6).

    O <CR>    FROM THE ON-LINE COMMAND STATE, THE CURRENT PROTOCOL
              MODE IS SET TO ORIGINATE.

    A <CR>    FROM THE ON-LINE COMMAND STATE, THE CURRENT PROTOCOL
              MODE IS SET TO ANSWER.

    H <CR>    FROM THE ON-LINE COMMAND STATE, THE MODEM WILL DISCONNECT
              FROM THE PHONE LINE AND RETURN TO LOCAL COMMAND STATE.

.PAŠRETURN STATUS CODES:

    CODE SEQUENCE                      FUNCTION
-------------------------------------------------------------------------

    0           MODEM READY - LOCAL COMMAND STATE

    1           DISCONNECT FROM PHONE LINE

    2           ON-LINE ORIGINATE

    3           NO ANSWER FROM REMOTE MODEM

    4           BUSY SIGNAL DETECTED

    5           NO CARRIER TONES

    6           DIAL TONE DETECTED

    7           NO DIAL TONE DETECTED

    8           MODEM READY - ON-LINE COMMAND STATE

    E           COMMAND ERROR

    C           RETURN TO COMMUNICATIONS MODE FROM ON-LINE COMMAND
 
    L           LOW SPEED (300 BAUD) 

   POWER ON-PARAMETER DEFAULTS

   N CODE       X VALUE              FUNCTION
-------------------------------------------------------------------------

    1             8            NUMBER OF RING BACKS

    2             0            SEND SPACE DISCONNECT OPTION IS OFF

    3           AUTO           9/10 BITS/CHARACTER

    4             0            AUTO ANSWER FUNCTION IS OFF

    5             5            BREAK SEQUENCE TIME INTERVAL