This article describes a table driven assembler I recently constructed
  to help with my  investigation  of  the  new  one  chip  microcomputers.   At
  present, my interest is in the Intel 8748 computer and the related Intel 8741
  Universal  Peripheral Interface, both with user programable EPROMs.  With the
  continued proliferation of new microprocessors, especially low end processors
  too small for resident utilities, I felt the best approach was a table driven
  cross-assembler.  Since my main system is an 8085-based system running  CP/M,
  I had a large choice of source languages for the assembler.  I uses ML-80 for
  several   reasons,   including   availability,   efficiency   and  structured
  programming features.  ML-80 is a structured  assembler/compiler  written  in
  1975 to combine the advantages of assembler level machine control with a good
  set of control structures to produce readable and efficient code.  I wrote it
  as  a  table  driven  compiler to make it easier to modify for use with other
  8-bit machines.  In particular, all components of an  operation  code  except
  immediate  operands  are  are  determined  by table lookup alone.  The target
  machines for the assembler listed  here  are  the  Intel  8748/8048/8035  and
  8741/8041.   A short companion article gives an explanation of the syntax and
  semantics of ML-80 as well as operational notes not widely published.  

                          General features of the Assembler

	 The  assembler  provides  as  basic  features  for  all  versions line
  parsing, symbol table management and expression evaluation.  The line  parser
  defines  a source line as a series of fields separated by blanks and tabs and
  terminated by CR/LF.  The first field is an optional label starting in column
  one, not over 6 characters long, optionally followed by a colon.  The  second
  field  is  an  operation  code  not over 5 characters.  The third field is an
  optional list of operands separated by commas.  The fourth field  treats  the
  rest  of  the  line  as  comments.  Note that for some operations some of the
  optional fields may actually be required.  To allow  for  longer  labels  and
  operations  requires  changing  the declarations for OP, LABELL, LABELTAB and
  adjusting the loop counters in  PARSELINE  and  GETNAMEVAL.   The  expression
  evaluator  recognizes  labels,  numbers  and '$' for the current value of the
  location counter (i.e.  the address of the instruction  containing  $).   ...
  Note  that  his routine had an error if the instruction is two bytes long, th
  has  now  been  fixed  (Trevor  Marshall).   Numbers  may  be   in   decimal,
  hexadecimal,  octal  or  binary,  denoted  by  a  suffix  of  D,  H,  O, or B
  respectively.  A number with no suffix is decimal.  The  first  character  of
  numbers  must  always  be  digits  to  distinguish  them  from  labels.   The
  expression evaluator also recognizes the operation symbols '+', '-', '>'  and
  '<' for plus, minus, low byte and high byte respectively.  When used as unary
  operations, the first operand is zero.  Low byte is the less significant byte
  of  the  following  value  and  high  byte is the more significant byte.  For
  example, >01234H is 34H and <01234H is 12H.  

                              Customizing the assembler

	 The behavior of the assembler is controlled by two main tables and two
  case statements (one in each pass).  The first table in the  listing  is  the
  operand  table from label RR1 through RR31.  This table is coded using macros
  RENTRY, RERROR, RNULL and RGO.  The second table is  in  the  declaration  of
  OTAB  immediately  after the operand table.  This table, constructed with the
  macro OENTRY, describes the operation codes for the assembler.  Each entry in
  this table gives an operation code, e.g.  'ORG',  the  base  value  for  this
  operation,  e.g.   '0', and names a starting point in the operand table, e.g.
  'RR30'.  Each operation is applied to a serial search of this  table  for  an
  exact  match (both length and contents), the operation value is saved and the
  operand pointer is used to start the search for operands.  The operand  table
  is  serially  searched  from the starting point given by the operation table.
  The operand table contains several kinds of entries, some of which  exist  to
  make  the  table  shorter  by sharing portions.  Entries created by the macro
  RENTRY result i.  comparison of the start of the operand field with the table
  entry.  An RENTRY consists of a match  string,  e.g.   'P1,#',  an  operation
  correction  value,  e.g.   '49'  meaning 49H, which is added to the opcode to
  produce the correct value for this operand, and a type  code,  e.g.   '[IM]',
  which  drives  the  case  clauses for operand format in the assembler.  These
  types are generated by macros which expand to small numbers.  The types which
  are currently defined are error, immediate byte follows, same page  branches,
  full  memory  call/jump,  psuedo  operation and operand complete.  The actual
  meaning of a type is defined by  the  case  statements  in  PASS1  and  PASS2
  described below.  

	 Entries  created  by  the macro RNULL are for operations which have no
  operands.  An entry of type RNULL is identical to RENTRY with  a  null  match
  string.   Since  the  search is for a match on the first few characters of an
  operand, if one operand form is a prefix of another for  the  same  operation
  (say  P  and  P3)  the  longer one should come first, otherwise both P and P3
  would match with P.  

	 Entries  created  by  the  macro  RGO  are  used to share parts of the
  operand lists.  An RGO entry gives  an  opcode  correction  value  and  names
  another  part of the operand table.  When the table lookup routines encounter
  an RGO entry, the search switches to the named part of the table after adding
  the correction value to the opcode.  This correction allows  for  differences
  in  the  spacing of different opcodes.  For example, the table entry RR4 ends
  with [RGO '60' '[RR3]'] because most of the possible operands for ADD are the
  same as for XCH, saving 10 entries.  RR3 is  part  of  another  space  saving
  technique.   RR3  is  an internal label of the declaration for RR1 (and RR2),
  thus, if the search falls through the entry after RR2, the effect is the same
  as [RGO '0' '[RR3]'] without the overhead.  RGO allows  several  variants  to
  join since only one can fall through, and also allows other variants by using
  opcode corrections.  

	 The  last  type of entry is generated by the RERROR macro.  This macro
  signals that the operand field does not contain a  valid  entry.   Note  that
  every path through the operand table must end with RERROR or RNULL.  

                                 PASS1 case statement

	 This  assembler  is  a  traditional  two pass assembler which resolves
  label values on the first pass and generates code on the second pass.   These
  two  passes are embodied in the procedures PASS1 and PASS2.  In each of these
  procedures, a case statement is driven by the results of  the  operand  table
  search.   In  pass  one,  the  case alternatives do processing to resolve all
  labels.  The basic function of pass one defines all  labels  as  the  current
  value of the location counter (the location counter is the assembler's analog
  of the processor's program counter).  The main function of the case statement
  is  to increment the location counter by the length of each instruction.  The
  second function is to  provide  special  processing  for  psuedo  operations.
  Psuedo  operation  processing  is  driven  by  a  second case statement.  The
  driving value for this case  statement  is  the  opcode  value  since  psuedo
  operations  don't generate an operation in the usual sense.  The case for EQU
  modifies the definition of its label to the value  of  the  expression.   The
  case  for  ORG  resets  the  location counter to its expression.  The DS case
  increments the location counter by the value of its expression.  

                                 PASS2 case statement

	 The main action in pass two is code generation by the different  cases
  with  appropriate  location  counter  adjustment (normally done by EMIT1, the
  subroutine which emits a byte of code), again with special  processing  in  a
  second case statement for pseudo-operations.  The calls to MAGNITUDEERROR are
  made  when  a two byte value is to be emitted in one byte but is not the sign
  extension of the single byte.

                              8741/8748 Assembler notes

	 The language currently recognized by the assembler is the union of the
  operations for the Intel 8741 and 8748,  and  the  appropriate  Intel  User's
  Manuals  are  the  primary  reference  on  valid  formats  and operands.  The
  operations are divided into four types for this assembler.  

	 Type 1.  This type is for operations with a single  immediate  operand
  data byte, for example ADD A,#5 

	 Type  2.   This  type  is  for the short conditional jump instructions
  which are limited to destinations on the same page (256 byte  block)  as  the
  next instruction, for example DJNZ R1,LOOP.  

	 Type  3.   This  type is for call and jump in which three address bits
  are part of the opcode and the remainder of the address is in a second byte.  

         Type 4.  This is a dummy type for psuedo operations.  These are 
                ORG     expression      ;set location counter to expression
        label   EQU     expression      ;equate label to expression
        [lab]   DS      expression      ;reserve expression bytes
        [lab]   DB      expression      ;define byte with value expression
                PRINT   ON               ;list assembly to printer
                PRINT   OFF              ;no listing (except errors)
	 Most of these  are  standard  pseudo  operations.   The  PRINT  pseudo
  operation  immediately  affects  the listing, making it possible to list only
  parts of an assembly.  The initial state of the assembler is PRINT ON.  

	 Type 5.  This case is for simple opcodes with operands included within
  a single byte, for example MOV A,@R1.  

                             Miscellaneous considerations

	 As compiled here, the assembler is limited to 255 labels by the  table
  size  declaration,  but  the search strategy is general enough for any length
  table.  To simplify I/O, the assembler also  presently  uses  the  fact  that
  there  is  only  1K of EPROM in an Intel 8748/8741, and first generates an in
  memory array of the result and finally writes a binary file  of  the  result.
  For  larger  memories, such as an 8080, EMIT1 needs to be revised to write to
  an output file, in a format such as Intel hex.  Since I wrote this on my CP/M
  system, the I/O used is specific to CP/M but has been carefully  encapsulated
  in only a few subroutines.  Procedure GETFC returns sucessive characters from
  the  input  file,  and  thus  is  responsible  for  reading  disk sectors and
  dribbling the contents out one character at a  time.   Procedures  PRINTALINE
  and PRMSG call CP/M BDOS to type characters on the console.  PRINTALINE lists
  lines  of  formatted  assembly output, while PRMSG types error messages.  The
  procedures ZTFCB, OPENR and OPENHEX also  perform  CP/M  specific  functions.
  These  procedures all assume the existence of a CP/M initialized file control
  block which CP/M has parsed the required file name from the command  invoking
  the  assembler.   For  another  DOS,  it  may be necessary to do this parsing
  separately, and change the format assumptions made by these routines.   ZTFCB
  initializes  a  file  control  block  prior  to  opening.  OPENR opens a file
  control block to read the source file, and is called  twice,  once  for  each
  pass.   OPENHEX  creates  a  new  file  with  suffix  SCC (now .COM -- Trevor
  Marshall) and writes the memory image buffer of the  assembled  code  out  in
  binary format.  Outside of these routines, the assembler makes no assumptions
  about  the  file  structures  available except that it is a sequence of bytes
  which can be read twice.  Conversion to another DOS should  be  fairly  easy,
  and conversion to a non-disk system should also be feasible.  

                                 Program availability

	 The  ML-80 compiler is part of the CP/M users group collection, and so
  is available from them.  The PL/M source for  ML-80  is  available  from  the
  Intel  Users'  Group.   As  an  alternative, for $10 I will provide a 8 inch,
  single density IBM format CP/M diskette with ML-80 and  the  source  for  the
  assembler in this article on it.