CPU280 System Software Information
                  ==================================
                      Tilmann Reh, 06 June 1993


                     System Software Version 1.1
                     ---------------------------

The  new system software release 1.1 for the CPU280 is offered  freely 
for  every  CPU280 owner or user. It is delivered as is,  without  any 
guarantees.  So everyone may have a look at the software and find  out 
what  he  has to change for getting it running with  his  environment. 
However,  I tried to make the new version as modular and  portable  as 
possible,  and  I  am always interested in receiving  bug  reports  or 
suggestions for later releases.

The  original system software delivered by me may be distributed  only 
complete.  The version message at signon must not be changed.  Changed 
versions  might  be further distributed, if it  is  stated  absolutely 
clearly that it is not the original version. Everyone who changes  the 
system  software code (not only disk parameters etc.) should  add  his 
initials  and  his  internal version number to the  BIOS  signon  (for 
example,  for the 5th change being made by me, the signon  could  read 
"V1.1tr5").

You may reach me using the following addresses:
     Tilmann Reh, In der Grossenbach 46, D-57072 Siegen
     Phone +49 271 312599, Fax +49 271 317359
     Internet: tilmann.reh@hrz.uni-siegen.dbp.de
Before July 1993, the above ZIP code must be replaced by "W-5900". The 
safest  way  to  reach me is regular mail -  fax  number  or  internet 
address may change.


This  document  describes major features of the  new  system  software 
release, especially implementing a particular harddisk drive.

P.S.:  Some users sometimes had problems to format diskettes with  the 
new system (although the Format Manager and it's BIOS interface wasn't 
changed).  Since I still don't know the cause of those  problems,  and 
didn't manage to reproduce them yet, I ask you to keep your eyes  open 
and inform me as soon as you experience some difficulties.



                         The modular approach
                         --------------------

The  new  system  introduces the concept of a  really  modular  driver 
structure  and all options being selectable by  conditional  assembly. 
The  modular driver structure applies especially to the disk  drivers, 
where  the only public label of each driver are the extended DPH's  of 
the  logical  drives.  The system kernel  addresses  the  driver  only 
through  the use of the drive table and these XDPH's, so  the  drivers 
should  be  freely exchangable, and it should be easy  to  create  new 
driver modules covering different hardware.
Since  all options are choosen by conditional assembly,  new  hardware 
support  routines  might simply be added to the original  source  code 
as  another option (please inform me about such expansions, so  I  can 
integrate them into further system software releases). For example,  a 
harddisk   driver  for  OMTI  controllers  (the  old   XT-type   8-bit 
controllers) will surely become another option in the HARD.280  module 
(the option file is already prepared for this).

The modular disk drivers also are already prepared for being used with 
the  next release of the boot loader program. For this  purpose,  they 
contain code which is needed only with the boot loader, code which  is 
needed  only with the system BIOS, and code which is needed for  both. 
This, too, is controlled via conditional assembly. There is an  option 
named LOADER, which is set true during assembly of the driver  modules 
for the loader program, and false during assembly of the system  BIOS. 
Since the option file is included in every source code module, we must 
have  different option files for the loader and the system  BIOS.  The 
appropriate  file (SYSTEM.LIB resp. LOADER.LIB) is then copied to  the 
file OPTIONS.LIB (which is included in every source module) every time 
the system BIOS or the loader program are assembled.

This is to give some information about the concept, and the meaning of 
the  new option files. Don't mess around with the LOADER flag! I  have 
not  yet started programming the new loader program, so it  will  last 
some  time  before it makes sense to ask me about.  However,  the  old 
loader  version  (1.02) will boot the new system from both  EPROM  and 
disk  without  any problems (even if the new system does not  use  all 
information the loader is offering).

                        Harddisk installation
                        ---------------------

One  of the great features of the system release 1.1 is  the  harddisk 
driver which allows for easy installation of IDE harddisks  (connected 
via my IDE interface board) by the use of macros. One needs to  change 
only  few  equations to get the new system running with  a  particular 
harddisk.

Every  harddisk is described by it's operating parameters,  which  are 
the number of cylinders, heads and sectors. The so-called native  mode 
of  IDE drives uses the physical parameters as  operating  parameters. 
Some  drives  support pseudo-native modes which have  some  parameters 
modified  by powers of two, for example twice the number of heads  and 
half  the  cylinder count. Many drives allow for free setting  of  the 
operating parameters and calculate the physical values internally,  as 
long  as  the  emulation fits into the total number  of  sectors  (the 
drive's capacity). These emulation modes (including pseudo-native) are 
for  the  "compatibility"  of the IBM  "clowns",  where  the  original 
harddisk controller WD 1010 could control only 1024 cylinders. So with 
modern  harddisks which have far more cylinders, these are  mapped  to 
logical drives with fewer cylinders.

Since I don't know for sure if modern IDE drives also mask the  higher 
bits of the cylinder register, you should also use an emulation  which 
has less than 1024 cylinders (logical). Pseudo-native modes are to  be 
preferred, since they probably are slightly faster. So, the first step 
is to fix the operating parameters of the drive.

The  next thing to do is the specification of the logical drives,  the 
partitions.  One physical harddisk drive may be splitted into  several 
logical  drives, so there are more separated areas to store files  in. 
Remember,  with  CP/M-3 you have only 16 user areas for  each  logical 
drive. So if you want to put all your files covering one theme into an 
own  area, you will need many partitions if you have many  themes.  To 
give  you an idea of the size of a partition: having files  of  normal 
size  (text files, programs, libraries, everything mixed), with  about 
100 files per drive/user area, this means about 1600 files per  drive, 
representing  about 10 to 15 megabytes. If you are planning  to  store 
large  files on one partition only, you might as well choose a  larger 
partition  for this purpose. If you want to have fewer files in a  d/u 
area, choose more smaller partitions (if possible).

The system software release 1.1 supports 9 harddisk partitions without 
changes.  By removing the optional semiconductor pseudo-drives  and/or 
unused  disk drives, you might get some more. Partition sizes  can  be 
defined by the number of cylinders.

After  you have defined how many partitions of which size you want  to 
install,  you must define the block size of each  partition.  Remember 
that you can allocate a maximum of 16 blocks to the directory. This is 
a very important limit! With 4k blocks, there are max. 2048  directory 
entries, enough for about 10-15 MB of mixed files when datestamping is 
used (highly recommended!). With greater blocks, you get more room for 
the  directory, while needing less - this is great! However,  blocking 
losses  rise as they are half the blocksize statistically (already  4k 
per  file when using 8k blocks). So you should choose the  block  size 
(and  the partition size) depending on the type of files you  want  to 
store in each partition. Then, the number of directory entries must be 
defined accordingly.

The  last  thing  to do is caused by the  16-bit  arithmetics  of  the 
assembler. I use an equation within a macro to calculate the number of 
blocks  in each partition. For partitions greater than or equal to  32 
MB,  an intermediate value will overflow and result in a  wrong  block 
count. So for every partition which is concerned, you have to do  this 
calculation  manually  and  enter the block count  directly  into  the 
source code.

These  are  the four things to do, with some information where  to  do 
them:

1. Fix the drive's operating parameters (cylinders, heads, sectors).
     The  operating parameters are defined in three equations  at  the 
     beginning of the HARD.280 module.

2. Define number and size of partitions.
     The  number  of  partitions  is  contained  in  the  option  file 
     SYSTEM.LIB  (!).  The  size of each  partition  is  defined  with 
     equations at the beginning of HARD.280.

3. Define the block size and directory capacity of each partition.
     The block size of each partition is defined immediately following 
     the partition size definition, at the beginning of HARD.280.  The 
     block  size is defined as number of sectors per  group  (=block), 
     where a sector is always 512 byte.
     The  number  of directory entries and  the  according  allocation 
     bytes must be defined directly within the DPB's, at the very  end 
     of  HARD.280. Partitions which are equal in capacity, block  size 
     and directory size, may share the same DPB. Change the number  of 
     different  DPB's to your requirements by adding or  removing;  be 
     sure to declare all needed DPB labels. Take care that if you have 
     too  much  DPB's, the resident BIOS portion will  need  3  memory 
     pages instead of two, reducing your TPA size by 256 byte.

4. Check for 32-MB overflows and correct manually.
     If there are partitions of 32 MB or greater, find the source code 
     line where the block count of each partition is calculated  (near 
     the  end  of HARD.280, within the IRPC macro). This  line  should 
     read:
          Blocks&i aset Part&i*Heads*Secs/SpG&i
     Add  a new line !after! this definition which contains the  right 
     value for the partition in question, for example:
          BlocksK aset 5036
     if your partition K is sized about 40 MB and uses 8k blocks. Take 
     care  to use an integer division which simply cuts the  remainder 
     (do not round!). 

One thing which I didn't mention yet: there's a signon message in  the 
harddisk  driver which is displayed after  successful  initialization. 
This  message  usually contains the harddisk's capacity and  the  used 
logical  drives (the letter from H: to anywhere). This message  should 
of course be adapted to the used harddisk and partitioning data.

After having created the new system file using the SYS make-file,  the 
GENCPM utility should be run manually in any case, explicitly checking 
the buffer sizes and definitions. Boot the new system from floppy disk 
first,  before burning it into EPROM's (BTW, the GENEPR utility  still 
works with the new system).

The  new  system  should be able to address  the  harddisk  partitions 
perfectly right from the start. If you experience any problems, please 
inform me about them as detailed as possible.

After  having booted the new system first, the directory structure  of 
all partitions must be created. For this, fill the complete  directory 
area with E5 bytes (for example using DU), except for the 60h position 
in  every  record which should be 21's (the latter can  also  be  done 
using the CP/M-3 command INITDIR). After that, use the SET command  to 
set  the  partition's directory label and activate the  date  stamping 
(create & update recommended).

                                ZPM 3
                                -----

There is a replacement for the CP/M-3 BDOS, written completely in  Z80 
code.  Thus,  it  is much more efficient and  also  offers  additional 
functions  compared  to the original CP/M-3.  Unfortunately,  it  also 
seems to contain some bugs and some mis-specifications (like  register 
usage  restrictions for the BIOS), at least in the actual release  09. 
Although I took care of the details I knew about ZPM3 when programming 
the  new BIOS, it still does not run error-free. Since the contact  to 
the  (australian)  author of ZPM3, Simeon Cran, has broken,  we  don't 
seem  to  have  the support needed to get it running.  If  we  someday 
receive  a  release of ZPM3 without those bugs, this BIOS  should  run 
with it without being changed.


- End of this document -